A90	PERFORMANCE SPECIFICATION GUIDANCE NOTES

CLAUSE GUIDANCE NOTES

All	Do not leave a clause in ‘Just in Case’, it will diminish the relevance of the specification to the job and undermine confidence in the specification by all readers of it.

If it might become relevant in the future, leave it out now, then edit the spec to add it back in and reissue it at the time.

Read the clauses every time you create a specification and if necessary edit it accordingly.

Do not accept a standard clause if it does not quite relate to your project, edit it accordingly.

If you are unsure how to edit it, seek advice.

GreenSpecCPD and GreenSpecConsult offer CPD, training and coaching on specification writing and editing.

4	Keep this clause in all cases

5 to 9P

If the list in each clause is not edited by the specifier (to suit the project scope of works, to update to current standards) then the clause(s) may be deleted and rely on clause 4.

9A	Applied to England, omit if project is elsewhere, edit as required,

9B	Applies to London, omit if project is elsewhere, edit as required,

9C	Applies to Scotland, omit if project is elsewhere, edit as required,

9D	Applies to Existing buildings with conservation quality repairs etc. omit if project is new, edit as required,

9E	Applies to any installation with connection to electrical, earthing or lightning protection systems, omit if not relevant

9F	Applies to structural applications of stainless steel, omit clause if not relevant,

9G	Applies to housing, omit clause if not relevant, edit list to suit.

9N	Edit to suit

HAPM (relates to Housing)

BPG (relates to Non-domestic)

BLP (relates to services)

9P	Edit to suit

106	Edit to suit

117	ENVIRONMENTAL PURCHASING POLICY: TRANSPORT

Background:

Under the Treaty of Rome and the Construction Products Directive, projects/tenders over a set value funded by Government or Public Bodies, must not create technical barriers to restrict the purchase of materials to local sources and must open purchasing up to manufacturers in other EU states to the benefit of the EU’s economy as a whole.

However this often leads to the creation of very open specifications and consequently materials are often being procured from outside the EU with no financial benefits for EU at all.

Case law has indicated that Environmental and Social issues may be taken into account in tender evaluations as long as requirements are included in the original specification.

The latest update of the EU Procurement Rules permit the inclusion of Social and Environmental requirements in Specification clauses.

Aim:

This project aims to address transport energy use and other environmental issues in its procurement policy.

To reduce carbon (CO2) emissions and embodied energy from transport using fossil fuel. E.g. Petrol, Diesel, Shipping oil, aeronautical fuel, etc.

Minimise the miles/kilometres supplies are transported throughout the whole extraction, transport, manufacturing processes and delivery to the site.

Requirements:

Purchase within the EU in preference to opening up to international suppliers.

Purchase from local manufacturers, in preference to regional, in preference to national, in preference to UK, in preference to EU mainland, in preference to global.

Support the local economy and local SME (Small to Medium Enterprise) manufacturers and tradesmen..

Wherever possible specify local, regional, national and EU products and manufacturers in the Specification for the above reasons.

Projects where procedural issues are covered in other parts of the Preliminaries or Contracts it may be safe to delete the following clauses:

92, 106, 120 – 138, 160 – 168, 170 – 179, 235 – 248, 281 – 284,

Projects where procedural issues are covered in other parts of the Preliminaries or Contracts can delete the following items from clauses:

11A	last two items

105A 	listed appendix

290	Edit to suit

291. 292, 293A, 294 - 297	For Housing, omit if not relevant, edit to suit

293B	For Non-domestic, omit if not relevant, edit to suit

296	For all building types, edit to suit

Some examples of replacement clauses

319A	FORCES from [MEWP Mobile Elevating Work Platforms on wheels and outrigger feet], working from the [Mall floors] are restricted to:

[Ground floor:

Italmec SEL 22/13: (Preferred)

Machine weight: 8500 kg.

Track: 2100 mm.

Wheelbase: 2350 mm.

Max. load on 2 adjacent wheels: 6800 kg.

Of which, max. load on 1 wheel: 5100 kg.

Spider TS/30 (Passes over Mall floor to get to Knuckles)

Machine weight: 5.6 Tonnes,

Width: 900 mm.

Length: 7400 mm.

Working: outrigger spacing  6000 x 6000 mm.

Max. load on 2 adjacent wheels: 4400 kg.

Maximum load on single outrigger 2900 kg.

Outrigger pad sizes: 300 x 400 mm.

Aerial B22T (undesirable)

Machine weight: 3000 kg

Track: 1800 mm.

Wheelbase: 3000 mm.

Working: outrigger spacing  4200 x 4700 mm.

Max. load on 2 adjacent outriggers 2400 kg.

Of which, max. load on 1 outrigger 1500 kg.

First Floor:

Aerial B18T (preferred)

Machine weight   2100 kg

Width     1600 mm.

Length    3000 mm.

Working: outrigger spacing  4200 x 4400 mm.

Max. load on 2 adjacent outriggers 2400 kg.

Of which, max. load on 1 outrigger 1500 kg.]

Assume that spreader plates below out rigger feet may not be used from time to time.

Uncontrolled impacts by machinery will be possible but the forces involved are more likely to cause excessive damage.

319B	ACCESS EQUIPMENT LOADINGS:

Forces on the floors will include pedestrian traffic and maintenance access equipment working from the [Rotunda Pavilion of the Bus Station floor] are restricted to either scaffolding on base plates or spreader boards or from [VPL Vertical Personal Lift on feet]:

[Ground floor:

Reference: Genie IWP - 305: (Preferred, confirm with CM),

Machine weight: 1390 lbs. 630 kg.

width (wide base): 1020 mm.

length (wide base): 1520 mm.

Max. capacity: 350 lbs. 159 kg.

Manufacturer: Genie Europe, Brunel Drive, Newark, Nottingham, NG24 2EG,

Tel: 01636 605030, Fax: 01636 611090.]

Assume that spreader plates below feet may not be used from time to time.

Uncontrolled impacts by machinery will be possible but the forces involved are more likely to cause excessive damage.

319C	ACCESS EQUIPMENT LOADINGS:

Forces from [MEWP Mobile Elevating Work Platforms on wheels and outrigger feet], working from the [East Village timber floors below external glazing] are restricted to:

[Ground floor:

Niftylift Height Rider 12 N: (below middle and northerly Icons in glazing).

Machine weight: 2950 kg. plus cage capacity 200 kg.

Width outer edge of tyres: 1500 mm.

Axle to axle: 1780 mm.

Max. load on 2 adjacent wheels: 1675 kg.

Of which, max. load on 1 wheel: 1890 kg.

Upright ULII Portable Personal lifts UL 48 (Use on mat well in southerly Icon and pass over timber floor):

Machine weight: 530 kg.

Width: 740 mm.

Length: 1250 mm.

Working: outrigger spacing  2850 x 2670 mm.

Max. load on 2 adjacent wheels: 318 kg.

Maximum load on single outrigger 371 kg.

Outrigger pad sizes: 100 mm. diameter].

Assume that spreader plates below out rigger feet may not be used from time to time.

Uncontrolled impacts by machinery will be possible but the forces involved are more likely to cause excessive damage.

630-639	Clauses created for the New British Library, if potentially relevant to a project may be edited or deleted.

Projects in Scotland Wales Jersey England, London: Edit the following clauses:

9B, 9C

Housing Projects

Keep the following clauses and edits to suit

A90	PERFORMANCE SPECIFICATION GUIDANCE NOTES

Clause(s) guidance notes on previous page(s)

© 1985-2012 ASWS NGS GreenSpec

REV	Revisions

| Revision No. | Description | Author | Date | Checked by: |
| --- | --- | --- | --- | --- |
| A00 | Extracted from A90 Spec file A08 update 25/04/2010 | BRM | 25/04/2010 |  |
| A01 | Updated URLs, revision table, file name, © start date | BRM | 08/12/2012 |  |
|  | Pending: Create more Guidance notes | BRM |  |  |

Terms and Conditions

1 The ‘Information’

1.1 The ‘Green Building Specification’ is a service provided by GreenSpec. These terms and conditions may be revised from time to time without prior notice.

1.2 This draft specification was prepared for the GreenSpec ‘Green Building Specification’ by Architectural Specification Writing Services (ASWS).

1.3 The specification clauses in this document (the 'Information') are based on past project work, information gathered from seminars, workshops and assimilated from published or unpublished verbal and written information.

1.4 The Information will continue to be developed and current files will be maintained on the GreenSpec website at www.greenspec.co.uk

2 Copyright Notice

2.1 Copyright and all other intellectual property rights in the Information shall remain at all times the property of GreenSpec and you shall acquire no rights in any such material except as expressly provided in this Agreement.

2.2 You are permitted to reproduce any part or parts either alone or in conjunction with your own material for the purposes of internal use in the your office, or for inclusion in any drawings or contract documents used or intended to be used in connection with a building contract where you are contracting party, or in connection with which you are engaged by one of the contracting parties in a professional capacity.

2.3 You shall not use, sell, assign, rent, sub-license, loan, or otherwise deal in any way in the Information or any interest in it except as expressly provided herein.

3 Disclaimer

3.1 Whilst GreenSpec endeavours to ensure that the Information is correct, it is provided on an "as is" basis, without warranties of any kind, and no warranty, express or implied, is given as to accuracy, currency or completeness and GreenSpec does not accept any liability for any error or omission. GreenSpec shall not be liable for any third party claims or losses of any nature including, but not limited to, loss of profits, direct, indirect, special or consequential damages arising from a third party's use or inability to use this Information.

3.2 All users and others must verify the contents of the Information and ensure that its application is effective to communicate what is required by them and that the Information is fit for their intended use which has not been specified by GreenSpec.

3.3 GreenSpec accepts no responsibility for the content on any internet website to which a hypertext link from this specification exists. The links are provided "as is" with no warranty, express or implied, for the information provided within them.

4 General

4.1 If any part of this Agreement is held by a court of competent jurisdiction to be unenforceable the validity of the remainder of the Agreement will not be affected.

4.2 This Agreement is covered by the Laws of England and Wales.

______________________________________________________

Addenda

NBS compatibility

National Building Specification (NBS) is the industry standard specification library.

GreenSpec’s Green Building Specification (GBS) is designed to complement NBS.

GreenSpec clauses are written specifically to address issues of environmental sustainability.

NBS adopts and develops the Construction Project Information Committee’s (CPIC) classification system Common Arrangement of Work Sections (CAWS) 1998 edition.

GBS adopts and develops the CPIC and NBS versions of CAWS to enable integration into NBS-based specifications.

GBS adopts NBS clause numbering to provide for easy clause assimilation.

CPIC: http://www.cpic.org.uk

CAWS: http://www.cpic.org.uk/en/publications/common-arrangement-listing.cfm

NBS: www.thenbs.com/

END	END OF A90	PERFORMANCE SPECIFICATION GUIDANCE NOTES