P14	Air/Wind tighT vapour permeable layer SYSTEMS

To be read with the Preliminaries/General conditions A10-A55 and A90 & A94.

GENERAL

5	BSI DOCUMENTS referred in or relevant: to work section P14 include:

BS 747:2000 Reinforced bitumen sheets for roofing

BS 3137:1972:Methods for determining the bursting strength of paper and board

BS 4255: Rubber used in preformed gaskets for weather exclusion from buildings

Part 1:1986:Specification for non-cellular gaskets .

BS 5250:2002:Code of practice for control of condensation in buildings

BS 5268:Part 1:1996 Structural use of timber.

BS 5534-1:2003:Code of practice for slating and tiling (including shingles)

BS 5925:1991:Code of practice for ventilation principles and designing for natural ventilation

BS 6399:Loading for buildings

BS 6399-2:1997:Code of practice for wind loads

BS 7386:1997:Specification for draught strips for the draught control of existing doors and windows in housing (including test methods)

BS 7543:1992 Guide to the durability of building elements, products and components.

BS 8000:Workmanship on building sites

BS 8000-6:1990:Code of practice for slating and tiling of roofs and claddings.

BS EN 1107-2 : 2001 Flexible sheets for waterproofing — Determination of dimension stability — Plastic and rubber sheets for roof waterproofing

BS EN 1928:2000:Flexible sheets for waterproofing — Bitumen, plastic and rubber sheets for roof waterproofing — Determination of watertightness

BS EN 12310-1 : 2000 Flexible sheets for waterproofing — Determination of resistance to tearing (nail shank) — Bitumen sheets for roof waterproofing

BS EN 12311-1 : 2000 Flexible sheets for waterproofing — Determination of tensile properties — Bitumen sheets for roof waterproofing

BS EN 13859-1:2005 Flexible sheets for waterproofing — Definitions and characteristics of underlay — Underlays for discontinuous roofing

BS EN 15026:2007:Hygrothermal performance of building components and building elements.  Assessment of moisture transfer by numerical simulation.

BS EN 20811:1992:Textiles — Determination of resistance to water penetration — Hydrostatic pressure test

BS EN ISO 12572:2001 Hygrothermal performance of building materials and products — Determination of water vapour transmission properties

5A	IS (IRISH STANDARDS) DOCUMENTS referred in or relevant: to work section P14 include:

IS EN 13829:2000:Thermal performance of buildings - Determination of air permeability of buildings - Fan pressurization method

ICP 2:2002 Irish code of practice for slating and tiling.

5B	DIN (GERMAN STANDARDS) DOCUMENTS referred in or relevant: to work section P14 include:

DIN 4102:1998-05:Fire behaviour of buildings and building components

DIN 4108:Thermal insulation and energy economy in buildings

DIN 4108-2:2003-07:Minimum requirements to thermal insulation

DIN 4108-7:2001-08:Airtightness of building, requirements, recommendations and examples for planning and performance

DIN 18160:Chimneys

DIN 18160-1:2006-01:Design and Performance

DIN EN 13984:2005-02: Flexible sheets for waterproofing - Plastic and rubber vapour control layers- Definitions and characteristics; (German version EN 13984:2004)

5C	CEN DOCUMENTS referred in or relevant: to work section P14 include:

EN 13788:2002:Hygrothermal performance of building components and elements - internal surface temperature to avoid critical surface humidity and interstitial condensation - Calculation methods

EN 13984:2005-02:Flexible sheets for waterproofing - plastic and rubber vapour control layers - Definition and characteristics

5D	ISO DOCUMENTS referred in or relevant: to work section P14 include:

BS EN ISO 12572:2001 Hygrothermal performance of building materials and products — Determination of water vapour transmission properties

BS EN ISO 14021:2001 Environmental labels and declarations. Self-declared environmental claims (Type II environmental labelling).

BS EN ISO 9001:2008:Quality management systems.  Requirements (formerly BS 5750:Part 1; =EN 29001 =ISO 9001)

6	AGRÉMENT DOCUMENTS referred in or relevant: to work section P14 include:

MOAT No. 69:2004:UEAtc Technical Report for the Assessment of Discontinuous Roofing Underlay Systems

Irish Agrément Certificate:

IAB 02/0138 Solitex Plus & Solitex UD Vapour Permeable Roofing Underlays for Pitched Roofs

IAB 07/0297 Pro clima intelligent airtight system (endorsed by NSAI)

British Board of Agrément Certificate:

BBA 07/4432 Pro clima Solitex Vapour permeable roofing underlay

7	UK REGULATORY & CITED DOCUMENTS: referred in or relevant: to work section P14 include: [

UK Building Regulations Approved Document L, L1A, L1B, L2A, L2B “Part L”

L1A	Conservation of Fuel and Power - New Dwellings 2006

L1B	Conservation of Fuel and Power - Existing Dwellings 2006

L2A	Conservation of Fuel and Power - New Buildings other than Dwellings 2006

L2B	Conservation of Fuel and Power - Existing Buildings Other Than Dwellings 2006

UK Building Regulations Approved Document F 2006 “Part F”

F	Means of Ventilation 2006

TGD Technical Guidance Document to Part F Technical Guidance Document

ATTMA TS1 2006:Air Tightness Testing & Measurement Association Technical Standard 1 Measuring Air Permeability of Building Envelopes]

7A	NON-UK REGULATORY & CITED DOCUMENTS: referred in or relevant: to work section P14 include: [

German Building Code EnEV Energy Saving Standard]

8	UK DESIGN STANDARDS & SOFTWARE referred in or relevant: to work section P14 include: [______]

8A	NON-UK DESIGN STANDARDS & SOFTWARE referred in or relevant: to work section P14 include:

Computer assisted simulation programme for heat and humidity transports (dynamic)

Standards: to BS EN 15026 accredited by [_______]

Product Reference: WUFI

W	www.wufi.de

8B	NON-UK DESIGN STANDARDS & SOFTWARE referred in or relevant: to work section P14 include:

Passivhaus Institute Germany:

Product Reference: PHPP Passivhaus Planning Package

W	www.passivhaus.de

8C	NON-UK DESIGN STANDARDS & SOFTWARE referred in or relevant: to work section P14 include:

Minneapolis Automated air test reports

Delphin

9A	OTHER UK DOCUMENTS referred in or relevant: to work section P14 include: [

BRE Airtightness in Commercial and Public Buildings

Energy Saving Trust:

Good Practice Guide:

GPG 224 Improving Airtightness in Dwellings

GPG:268 Energy Efficient ventilation in Dwellings – a guide to specifiers]

9B	BSRIA BUILDING SERVICES RESEARCH & INFORMATION ASSOCIATION DOCUMENTS referred in or relevant to preliminaries section P14 include: [

11/2004 Airtightness testing for new dwellings: A practical guide for Builders and testers

07/1999 Envelope Integrity Demonstration Study (I N Potter)

10/1998 Airtightness Specification

BSRIA, Air tightness for Building Regulations]

9C	OTHER NON-UK DOCUMENTS referred in or relevant: to work section P14 include:

Swiss Standards:

SIA 180:01-2000:Protection against heat loss and humidity control in buildings

Austrian Standards:

ÖNorm B8110-2:Thermal insulation in building construction

ÖNorm B8110-2:2003-07-01:Water vapour diffusion and protection against condensation

Accreditation: CE Mark in accordance with DIN EN 13984

DIBt Approved as a construction product according to the German Construction Product List C.

Sentinel House German indoor air quality standard

AHFC Alaska Housing Finance Corporation: BEES Building Energy Efficiency Standards 2002

10	MANUFACTURERS DOCUMENTS referred in or relevant: to work section P14 include: [

Pro clima: Calculating potential freedom from structural damage of thermal insulation, Structures in timber built systems 02/2005

Pro clima Intelligent Airtight and Windtight building systems Product Portfolio (not dated, published 2009)

Pro clima INTELLO High performance intelligent vapour check Application Guide (vh_intello_11.07)

Pro clima System Interior Insulation INTELLO 11.2008]

11	RELATED WORK SECTIONS:

Refer to the following work sections for additional requirements pertaining: to work section P14

A90	PERFORMANCE SPECIFICATION

A94	ON SITE TESTING

G20	CARPENTRY/TIMBER FRAMING/FIRST FIXING

H92	RAINSCREEN CLADDING/OVERCLADDING

H60	PLAIN ROOF TILING

H61	FIBRE CEMENT SLATING

H62	NATURAL SLATING

H63	RECONSTRUCTED STONE SLATING TILING

H64	TIMBER SHINGLING

H65	SINGLE LAP ROOF TILING

H66	BITUMINOUS FELT SHINGLING

H70	MALLEABLE METAL SHEET PRE-BONDED COVERINGS CLADDING

H71	LEAD SHEET COVERINGS/FLASHINGS

H72	ALUMINIUM SHEET COVERINGS/FLASHINGS

H73	COPPER SHEET COVERINGS/FLASHINGS

H74	ZINC SHEET COVERINGS/FLASHINGS

H75	STAINLESS STEEL SHEET COVERINGS/FLASHINGS

H76	FIBRE BITUMEN THERMOPLASTIC SHEET COVERINGS FLASHINGS

H92	RAINSCREEN CLADDING/OVERCLADDING

M20	PLASTERED/RENDERED/ROUGHCAST COATINGS

P10	SUNDRY INSULATION/TIGHTNESS WORK/FIRE STOPS

P11	FOAMED/FIBRE/BEAD CAVITY WALL INSULATION

12	SCOPE OF WORK:

The Works consist of: Design/design development, manufacture, supply, delivery, installation of air and wind tightness layers together with all materials and components necessary to achieve the required performance and provide an installation fit for its intended purpose, all in accordance with the design-intent Drawings and this Specification.

In particular carryout the following:

[Drawings: develop the details, membrane, batten and joint layouts of the installation,

Services interfaces with membranes

Specification of each membrane, adhesive tape and adhesive, etc.

SYSTEMS

110	AIR TIGHTNESS & HUMIDITY VARIABLE VAPOUR CHECK LAYER TO EXTERNAL ENVELOPE:

Reference Drawing(s): [______],

Location: [________],

Background: [________],

Preceding trades:

External wind tightness system: to P14/110

Thermal insulation between framing: See P10/____]

Membrane: [________],

Adhesive(s): [________],

Adhesive tape(s): [________],

Corner sealing: [________],

Cable penetration grommet(s): [________],

Pipe penetration grommet(s): [________],

Insulation injected hole repair: [________],

Damage repair: [________],

Fasteners: [________],

Tools: [________],

Battens: [________],

Code of Practice: [See P14/500A]

Approved installers: [________],

Workmanship: [________],

Completion:

Testing: to P14/910 - P14/960 and work section A94

Test level: [__] air changes per hour @ 50 pascals

Test Report: to P14/950

Certificate: to P14/960

Following trades:

Outside of timber framing and thermal insulation:

Breather membrane to P10/___]

Roofing underlay: to work section H60-H66]

Wind-tightness membrane/Insulation protection layer: to P14/110A

Wood fibre thermal insulation to P10/___]

Breathing sheathing board to P10/___]

Sarking boarding: wooden planking to G20/___]

Inside of timber framing and thermal insulation:

Plasterboard dry lining: to work section K10

Linings: to work section K11

Fine linings: to work section K13

110A	AIR TIGHTNESS LAYER & HUMIDITY-VARIABLE ‘INTELLIGENT’ VAPOUR CHECK:

Reference Drawing(s): [______],

Location: [

External Envelop

Inside face of insulated pitched roofs

Underside face of timber joisted flat roof, using timber or proprietary timber sections,

Inside face of external stud walls, using timber or proprietary timber sections,

Ceilings

Floors

Underside of floors and ceilings,

Wet-rooms.  Kitchens, showers & bathrooms in domestic buildings,

Background: [Softwood framing at 600 mm. centres],

Preceding trades: [

External wind tightness layer: to P14/110A

Thermal insulation: to P10/____]

Membrane: [

Generally: Pro clima DB+: to P14/311A or Pro clima Intello Plus: to P14/310AGood indoor air quality & Eco Projects: Pro clima DB+: to P14/311AWet-rooms: kitchens, shower and bathrooms: Pro clima Intello Plus: to P14/310A]Adhesive(s): to P14/320A – P14/322A

Adhesive tape(s): to P14/330A, P14/332A, P14/334A, P14/335A

Corner sealing: to P14/336A

Cable penetration grommet(s): to P14/340A – P14/342A

Pipe penetration grommet(s): to P14/343A - P14/344A & P14/345A

Insulation injected hole repair: to P14/350A, P14/680 & P14/685

Damage repair: to P14/331A

Fasteners: Staples: to P14/410A

Tools: to P14/390A

Noggins and Battens:

Lap joint support noggins: to P14/420A

Service zone battens: to P14/423A

Code of Practice: [See P14/500A]

Agrément Certificate: Irish Agrément Board Certificate: IAB 07/0297 Pro clima intelligent airtight system

Manufacturer’s recommendations: to P14/502

Approved installers: to P14/508K

Workmanship: to P14/540 - P14/695

Completion:

Testing: to P14/910 - P14/960 and work section A94

Test level: [__] air changes per hour @ 50 pascals

Test Report: to P14/950

Certificate: to P14/960

Following trades:

Outside the timber framing and thermal insulation:

Breather membrane: to P10/___]

Roofing underlay: to work section H60-H66]

wind-tightness membrane/Insulation protection layer: to P14/110A

wood fibre thermal insulation: to P10/___]

breathing sheathing board: to P10/___]

Sarking boarding: wooden planking: to G20/___]

Inside the timber framing and thermal insulation:

Plastering in onto fleece strip by others: See work section M20

Drylining by others: See work section K10

111	AIR TIGHTNESS & HUMIDITY VARIABLE VAPOUR CHECK LAYER WITH BLOWN IN INSULATION:

Reference Drawing(s): [______],

Location: External envelop,

Background: timber framed wall/pitched roof with blown-in insulation

Preceding trades: External wind tightness layer See P14/110_]

Membrane: [________],

Adhesive(s): [________],

Adhesive tape(s): [________],

Corner sealing: [________],

Cable penetration grommet(s): [________],

Pipe penetration grommet(s): [________],

Insulation injected hole repair: [________],

Damage repair: [________],

Fasteners: [________],

Tools: [________],

Battens: [________],

Code of Practice: [See P14/500A]

Approved installers: [________],

Workmanship: to P14/[________] – P14/[________],,

Completion:

Testing: to P14/910 - P14/960 and work section A94

Test level: [__] air changes per hour @ 50 pascals

Test Report: to P14/950

Certificate: to P14/960

Following trades: [______].

111A	AIR TIGHTNESS & HUMIDITY VARIABLE VAPOUR CHECK LAYER  WITH BLOWN IN INSULATION:

Reference Drawing(s): [______],

Location: [

Inside face of insulated pitched roofs

Underside face of timber joisted flat roof, using timber or proprietary timber sections,

Inside face of external stud walls, using timber or proprietary timber sections,

Ceilings

Floors

Underside of floors and ceilings,

Wet-rooms.  Kitchens, showers & bathrooms

High humidity rooms]

Background: [Softwood framing at 600 mm. centres],

Preceding trades:

External wind tightness layer See P14/110A

Plaster undercoat, See M20/____]

Membrane: [

Generally:

Pro clima DB+: to P14/311A or Pro clima Intello Plus: to P14/310A

Eco Projects: Pro clima DB+: to P14/311A

Wet-rooms: kitchens, shower and bathrooms: Pro clima Intello Plus: to P14/310A]

Adhesive(s): to P14/320A – P14/322A

Adhesive tape(s): to P14/330A – P14/335A

Corner sealing: to P14/336A

Cable penetration grommet(s): to P14/340A – P14/342A

Pipe penetration grommet(s): to P14/343A - P14/344A & P14/345A

Insulation injected hole repair: to P14/350A, P14/680 & P14/685

Damage repair: to P14/331A

Fasteners: to P14/410A

Tools: to P14/390A

Noggins and Battens:

Lap joint support noggins: to P14/420A

Pressure & support battens: to P14/421A

Service zone battens: to P14/423A

Code of Practice: [See P14/500A]

Agrément Certificate: Irish Agrément Board Certificate: IAB 07/0297 Pro clima intelligent airtight system

Manufacturer’s recommendations: Comply.

Approved installers: to P14/508K

Workmanship: to P14/540 - P14/690

Completion:

Testing: to P14/910 - P14/960 and work section A94

Test level: [__] air changes per hour @ 50 pascals

Test Report: to P14/950

Certificate: to P14/960

Following trades:

Outside the timber framing and thermal insulation:

Breather membrane to P10/___]

Roofing underlay: to work section H60-H66]

wind-tightness membrane/Insulation protection layer: to P14/110A

wood fibre thermal insulation to P10/___]

breathing sheathing board to P10/___]

Sarking boarding: wooden planking to G20/___]

Between timber framing:

Blown in insulation: See work section P11, P11/___]

Inside of timber framing and thermal insulation:

Plasterboard dry lining: to work section K10

Linings: to work section K11

Fine linings: to work section K13

Plaster finishing coat in onto fleece strip by others See work section M20.

112A	WIND TIGHT VAPOUR PERMEABLE PITCHED ROOF UNDERLAY:

Reference Drawing(s): [______],

Location: Pitched roofs above rafters

Preceding trades: Timber framing see work section G20

Background: Pitched roof softwood rafters at 600 mm. centres

Membrane: Pro clima DA 3 layer to P14/314A

Adhesive(s): Orcon F to P14/322A,

Adhesive tape(s): Tescon No. 1 to P14/332A, Contega PV to P14/334A or Duplex to P14/335A

Corner sealing: Tescon Profil to P14/336A

Cable penetration grommet(s): to P14/340A – P14/342A

Pipe penetration grommet(s): to P14/343A - P14/344A & P14/345A

Damage repair: to P14/331A

Fasteners: to P14/410A

Tools: to P14/390A

Code of Practice: [See P14/500A]

Approved installers: to P14/508K

Workmanship: to P14/540 - P14/695

Completion:

Testing: is not possible

Following trades:

Above rafter thermal insulation to P10/___]

External wind tightness layer See P14/110, 110A,

Outside the timber framing and thermal insulation:

Breather membrane: to work section P10, P10/___]

Roofing underlay: to work section [H60-H66]

wind-tightness membrane/Insulation protection layer: to P14/110A

wood fibre thermal insulation to P10/___]

breathing sheathing board to P10/___]

Sarking boarding: wooden planking to G20/___]

Inside of timber framing and thermal insulation:

Plasterboard dry lining: to work section K10

Linings: to work section K11

Fine linings: to work section K13

Plastering in onto fleece strip by others See work section M20.

113A	WIND TIGHT VAPOUR PERMEABLE FLAT METAL ROOF UNDERLAY:

W	http://www.proclima.com/co/FRN/fr/solitex_um_connect_prod_fr.html (French)

W	http://www.proclima.co.nz/solitex-um-connect (English)

Product Reference: Solitex UM

115	TIMBER PANEL AIR TIGHTNESS LAYER TO EXTERNAL ENVELOPE:

Reference Drawing(s): [______],

Location: [________],

Background: [________],

Preceding trades:

External wind tightness system: to P14/110

Thermal insulation between framing: See P10/____]

Timber panel: [________],

Fasteners: [________],

Adhesive tape(s): [________],

Corner sealing: [________],

Cable penetration grommet(s): [________],

Pipe penetration grommet(s): [________],

Tools: [________],

Noggins and Battens: [________],

Code of Practice: [See P14/500A]

Agrément Certificate: Irish Agrément Board Certificate: IAB 07/0297 Pro clima intelligent airtight system

Manufacturer’s recommendations: to P14/502

Approved installers: [________],

Workmanship: [________],

Completion:

Testing: to P14/910 - P14/960 and work section A94

Test level: [__] air changes per hour @ 50 pascals

Test Report: to P14/950

Certificate: to P14/960

Following trades:

Outside of timber framing and thermal insulation:

Breather membrane to P10/___]

Roofing underlay: to work section H60-H66]

Wind-tightness membrane/Insulation protection layer: to P14/110A

Wood fibre thermal insulation to P10/___]

Breathing sheathing board to P10/___]

Sarking boarding: wooden planking to G20/___]

Inside of timber framing and thermal insulation:

Plasterboard dry lining: to work section K10

Linings: to work section K11

Fine linings: to work section K13

115A	TIMBER PANEL AIR TIGHTNESS LAYER TO EXTERNAL ENVELOPE:

Reference Drawing(s): [______],

Location: [

External Envelop

Inside face of insulated pitched roofs

Underside face of timber joisted flat roof, using timber or proprietary timber sections,

Inside face of external stud walls, using timber or proprietary timber sections,

Ceilings

Floors

Underside of floors and ceilings,

Wet-rooms. Kitchens, showers & bathrooms in domestic buildings,

Background: [Softwood framing at 600 mm. centres],

Preceding trades: [

External wind tightness layer: to P14/110A

Thermal insulation: to P10/____]

Timber panel: [________],

Fasteners: [________],

Adhesive tape(s): to P14/330A, P14/332A,  P14/334A and P14/335A

Corner sealing: to P14/336A

Cable penetration grommet(s): to P14/340A – P14/342A

Pipe penetration grommet(s): to P14/343A - P14/344A & P14/345A

Tools: to P14/390A

Noggins and Battens:

Pressure battens: to P14/421A

Service zone battens: to P14/423A

Code of Practice: [See P14/500A]

Agrément Certificate: Irish Agrément Board Certificate: IAB 07/0297 Pro clima intelligent airtight system

Manufacturer’s recommendations: to P14/502

Approved installers: to P14/508K

Workmanship: to P14/540 - P14/695

Completion:

Testing: to P14/910 - P14/960 and work section A94

Test level: [__] air changes per hour @ 50 pascals

Test Report: to P14/950

Certificate: to P14/960

Following trades:

Outside the timber framing and thermal insulation:

Breather membrane: to P10/___]

Roofing underlay: to work section H60-H66]

wind-tightness membrane/Insulation protection layer: to P14/110A

wood fibre thermal insulation: to P10/___]

breathing sheathing board: to P10/___]

Sarking boarding: wooden planking: to G20/___]

Inside the timber framing and thermal insulation:

Plastering in onto fleece strip by others: See work section M20

Plasterboard dry lining: to work section K10

Linings: to work section K11

Fine linings: to work section K13

120	WINDTIGHT VAPOUR PERMEABLE PITCHED ROOF UNDERLAY & INSULATION PROTECTION LAYER:

Reference Drawing(s): [______],

Location: [________],

Background: [________],

Preceding trades: Thermal insulation between framing: See P10/____]

Membrane: [________],

Overlaps: [________] minimum

Roof Pitch 	Horizontal lap 		Horizontal lap	Vertical lap

Partially Supported 	Fully Supported

<22.5o		225 mm.			100 mm.		100 mm.

>22.5o <35o	150 mm.			100 mm.		100 mm.

>35o		100 mm.			75 mm.		100 mm.

Adhesive(s): [________],

Adhesive tape(s): [________],

Corner sealing: [________],

Cable penetration grommet(s): [________],

Pipe penetration grommet(s): [________],

Damage repair: [________],

Fasteners: [________],

Tools: [________],

Battens: [________],

Incorporated items: [________],

Code of Practice: [See P14/500A]

Approved installers: [________],

Workmanship: [________],

Completion:

Testing: to P14/910 - P14/960 and work section A94

Test level: [__] air changes per hour @ 50 pascals

Test Report: to P14/950

Certificate: to P14/960

Following trades: [_______].

120A	WINDTIGHT VAPOUR PERMEABLE PITCHED ROOF UNDERLAY & INSULATION PROTECTION LAYER:

Reference Drawing(s): [______],

Location: Pitched roofs above rafters and sarking boards/insulation boards

Do not use in flat roofs

Background: Pitched roof softwood rafters at 600 mm. centres

Preceding trades:

Timber framing to BS 5268:Part 1, see work section G20

Breather membrane to P10/___]

Wood fibre thermal insulation to P10/___]

Breathing sheathing board to P10/___]

Sarking boarding: wooden planking to G20/___]

Membrane:

Pro clima Solitex Plus: to P14/317A

Overlaps: (Minimum)

Roof Pitch 	Horizontal lap 		Horizontal lap	Vertical lap

Partially Supported		Fully Supported

<22.5o		225 mm.			100 mm.		100 mm.

>22.5o <35o	150 mm.			100 mm.		100 mm.

>35o		100 mm.			75 mm.		100 mm.

Battens: to P14/424A

Adhesive(s): Orcon F: to P14/335A,

Adhesive tape(s):

to overlaps: Tescon No.1: to P14/332A

Corner sealing: Tescon Profil: to P14/336A

Cable penetration grommet(s): to P14/340A – P14/342A

Pipe penetration grommet(s): to P14/343A - P14/344A & P14/345A

Damage repair: Tescon No. 1: to P14/332A

Fasteners: to P14/411A

Tools:

Pressing aid: to P14/390A

Stapler: to P14/394A

Code of Practice: install in accordance with: ICP 2:2002, BS 5534-1:2003 and BS 8000-6:1990

Standard: Exceeds Type 1F reinforced bitumen underlay to BS 747:2000

Approved installers: to P14/508K

Workmanship: to P14/710 - P14/770

Following trades:

Outside the timber framing and thermal insulation:

Roofing battens and tiling/slating: to work section H60-H66]

PV, PVT, ST tiles: to work section [___]

Inside of timber framing and thermal insulation:

between rafter thermal insulation: to work section P10, P10/___]

Blown-in thermal insulation: to work section P11, P11/___]

Internal air tightness layer: to P14/120, 120A, 121, 121A

Plasterboard dry lining: to work section K10

Linings: to work section K11

Fine linings: to work section K13

120B	 WIND TIGHT & VAPOUR PERMEABLE UNDERLAY:

Reference Drawing(s): [______],

Location:

Outer edges of timber floors in platform floor construction

Outer edge of precast concrete hollow plank floors

Background & Preceding trades:

Double softwood joists Timber floor to BS 5268:Part 1, see work section G20

Precast concrete floor edge,

Membrane:

Pro clima Solitex Plus: to P14/317A

Profile: top hat section on side

Width = (Width of external wall x 2) + Depth of floor + ([75] mm. x 2)

Overlaps: (Minimum) [____] mm.

Installation: apply to edge of floor before being offered up to timber framing ensure extending lips are kept clear and not trapped.

Lapping: lips to extend upwards and downwards to lap with internal membranes on external walls.

Adhesive(s): Orcon F: to P14/335A,

Adhesive tape(s): to overlaps

Tescon No.1: to P14/332A

Corner sealing: Tescon Profil: to P14/336A

Cable penetration grommet(s): to P14/340A – P14/342A

Pipe penetration grommet(s): to P14/343A - P14/344A & P14/345A

Damage repair: Tescon No. 1: to P14/332A

Fasteners: to P14/411A

Tools: to P14/390A & P14/392B

Code of Practice: [See P14/500A]

Standard: [_____]

Approved installers: to P14/508K

Workmanship: to P14/710 – P14/770.

Following trades:

Outside the timber framing and thermal insulation:

Thermal insulation to P10/____]

Tile hanging battens and tiling/slating: to work section [H60-H66]

Metal cladding battens: to work section H7_]

PV, PVT, ST tiles: to work section [___]

Inside of timber framing and thermal insulation:

between rafter thermal insulation: to work section P10, P10/___]

Blown-in thermal insulation: to work section P11, P11/___]

Internal air tightness layer: to P14/120, 120A, 121, 121A,

Plasterboard dry lining: to work section K10

Linings: to work section K11

Fine linings: to work section K13

140	WINDTIGHT VAPOUR PERMEABLE FACADE UNDERLAY & INSULATION PROTECTION LAYER:

Reference Drawing(s): [______],

Location: [______],

Background: [______],

Preceding trades: [______],

Membrane: [______],

Overlaps: (Minimum): Horizontal lap: [___] mm.	Vertical lap: [____] mm.

Adhesive tape(s): [______],

Cable penetration grommet(s): to P14/340A – P14/342A

Pipe penetration grommet(s): to P14/343A - P14/344A & P14/345A

Damage repair: [________],

Fasteners: to P14/411A

Tools:

Pressing aid: to P14/390A

Stapler: to P14/394A

Code of Practice: [See P14/500A]

Standard: Exceeds Type 1F reinforced bitumen underlay to BS 747

Approved installers: to P14/508K

Workmanship: to P14/710 - P14/770

Battens: to P14/424A

Following trades:

Outside:

Cladding hanging battens and tiling/slating: to work section H60-H66

Metal cladding to work section H70-H76

Rainscreen cladding to work section H92

PV, PVT, ST tiles: to work section [___]

Inside of masonry:

Inside of timber framing and thermal insulation:

between rafter thermal insulation: to work section P10, P10/___]

Blown-in thermal insulation: to work section P11, P11/___]

Internal air tightness layer: to P14/120, 120A, 121, 121A

Plasterboard dry lining: to work section K10

Linings: to work section K11

Fine linings: to work section K13

PRODUCTS

310A	 AIR TIGHT & HUMIDITY-VARIABLE VAPOUR CHECK MEMBRANE:

System: Complete intelligent air-tightness system with all necessary adhesive agents.

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Reference: Pro clima Intello Plus

Accreditation:

CE Mark in accordance with DIN EN 13984

NSAI Agrément Certificate: NSAI 07/0297

Importing Agents: Ecological Building Systems See P14/509K

UK & Ireland Agent: Ecological Building Systems UK Ltd. See P14/509K

Product Page: http://www.greenspec.co.uk/html/product-pages/intello_plus.php

Properties: Airtight and vapour permeable, easy to apply, no splicing or tear propagation due to reinforcing layer.

Breaking Load:

MD: 425 N/50mm.

CD: 280 N/50mm.

Durability: to EN 13984

Application:

Internal face only

Roofs, walls & floors

Difficult to protect against condensation: Flat roofs, flexible metal sheeting

Fire Rating E

Material: 100 % polyolefins,

Membrane: Polyethylene copolymer

Fleece: Polypropylene

Reinforcement layer: Polypropylene

Manufacture: assembled by extrusion coating process involving heat and pressure.

Colour: Translucent, white with black and green text or markings

These materials allow for easy recycling.

Water Vapour Transmission Resistance:

sd: <0.25 m to >10.5 m (humidity variable)

Permeance : >13.2 to <0.33 US perms

MVTR: humidity-variable range: <1.28 to >51 MNs/g

Temperature resistance: -40 to +80 degrees C

Diffusion resistance factor: 37.500

Standard dew point assessment/calculation to BS EN 13788

Thickness: 0.2 mm.

Surface weight: 125 g/m2.

Roll size: 1500 mm. x 20 or 50 m. (standard sizes, others available subject to order, upon request)

Environmental Credentials:

Country of origin and manufacture: Germany,

Attributes:

Diffusion Open product for use in breathing construction,

Use with the following sealing adhesive tapes and adhesives:

Adhesives: Orcon F to P14/322A

Adhesive tapes:

Unitape to P14/330A

Tescon No. 1 to P14/336A

311A	AIR TIGHT & HUMIDITY VARIABLE PERFORMANCE VAPOUR CHECK MEMBRANE:

System: Complete intelligent air-tightness system with all necessary adhesive agents.

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Reference: Pro clima DB+,

Importing Agents: Ecological Building Systems See P14/509K

UK & Ireland Agent: Ecological Building Systems UK Ltd. See P14/509K

Product Page: http://www.greenspec.co.uk/products/air-tightness-membranes/pro-clima-DB%20plus/

3rd party Certification:

natureplus Certificate No.: 1701_0901_083_1 Valid until Jan 2012

NSAI Agrément Certificate: NSAI 07/0297

CE Mark in accordance with DIN EN 13984

Properties:

Breaking Load:

MD: 550 N/50mm

CD: 310 N/50mm

Durability: to EN 13984

Application:

Internal face only,

ecological and good indoor air quality projects,

Protection for thermal insulation systems against penetrating moisture, damage and mould.

Reduction in cold air penetration and hot air loss, reducing energy in use of the building and CO2 emissions.

Airtight and vapour permeable,

Reduces risk of interstitial condensation in summer and winter

Permits vapour to escape internally from constructions with vapour impermeable materials externally

Humidity-variable diffusion resistant membrane

Water Vapour Transmission Resistance:

sd: (Humidity variable) 0.60 m to 4 m (2.3 m)

Standard dew point assessment/calculation to BS EN 13788

Permeance: 5.4 to 0.82 US perms

MVTR: <3.06 to >20.4 MNs/g

Surface weight: 185 g/m2

Vapour diffusion resistance: 10 MNs/g at an average humidity of 60% (room 70%, construction 50%)

Fire class: E, treated with natural salts against fire

Temperature resistance: Long-lasting up to -40° C to + 80° C

Tear resistant due to reinforcement.

Environmental Credentials:

Country of origin and manufacture: Germany,

Diffusion Open product for use in breathing construction,

Natural content: cellulose fibre paper,

Recycled content: cellulose fibre paper 50 % to ISO 14021

Recyclable.

Material: natural and recycled cellulose fibre Kraftpaper, glued with a thin halogen-free and plasticiser-free PE Polyethylene film, plastic mesh reinforced for additional strength and treated with natural salts against fire

Thickness: 0.23 mm.

Roll size: 1350 mm. x 50 m. (standard size, others available subject to order, upon request)

Accreditation: CE Mark in accordance with DIN EN 13984

The membrane has no front and back side and can be fitted with either the printed or the unprinted side facing the room.

The printed markings are only an aid to orientation.

Use with the following sealing adhesive tapes and adhesives:

Adhesives:

Ecological and good indoor air quality Pro clima Eco Coll to P14/320A

Pro clima Orcon F to P14/322A

Adhesive tapes:

Unitape to P14/330A

Tescon No. 1 to P14/336A

314B	AIR TIGHT VAPOUR CHECK VAPOUR CHECK SEALING STRIP:

System: vapour check air-tightness sealing strip with all necessary adhesive agents.

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Reference: Pro clima DA-S

Accreditation:

CE Mark in accordance with DIN EN 13984

IAB Certificate 07/0297 Pro clima intelligent airtight system

Importing Agents: Ecological Building Systems See P14/509K

Backgrounds: Plywood, chipboard, OSB, concrete, timber, membranes,

Applications:

Internal only

Airtight sealing strip at critical junctions between building materials:

(e.g. OSB to concrete) in accordance to DIN 4108,

For roof, roof slopes, walls and floors,

Eaves and gables,

Skirting junction with floor

Large gaps at junctions to windows and doors

Materials with short term moisture penetration

Properties:

Weatherproof, water repellent and water resistant

Air tight sealing layer and generally applied on the inside of insulation

Fire Rating E

Material: made up of two layers

Robust polypropylene protection fleece, Halogen free polypropylene film

Temperature resistance: -40 degrees C to +90 degrees C

Life expectancy: 60 years +

Roll size: 210 mm. x 100 m.

Environmental Credentials:

Country of origin and manufacture: Germany,

Attributes:

Vapour check and airtight,

Site issues:

Protects the building from the weather during construction

Protecting structure during construction phase

More resistant to site conditions than other vapour checks

Can be exposed to the elements for 4 months.

When applied externally it is not possible to perform quality control testing either using a pressure differential method such as using the Pro clima Wincon see P14/690 or by means of a visual test, such as the Blower Door See P14/910 & 970

It is therefore imperative that all taping and attachment is done with utmost care.

Ensure detailed planning, particularly of fitting at the eaves and gables,

Ensure careful execution when fitting insulation over rafters.

Use with:

Adhesives: Pro clima Orcon F: to P14/322A,

Adhesive tapes: Tescon No. 1 to P14/332A,

Tools: Double dispensing gun: to P14/392A.

Delay between taping/sealing and air testing: Generally: 10 minutes minimum.

316A	WIND TIGHT & AIRTIGHT VAPOUR PERMEABLE PITCHED ROOF UNDERLAY:

System: Complete roofing tile underlay vapour permeable, airtight, windtight system with all necessary adhesive agents.

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Reference: Pro clima Solitex UD

Accreditation: CE Mark in accordance with DIN EN 13984

Irish Agrément Certificate:

IBA 02/0138 Solitex Plus & Solitex UD Vapour Permeable Roofing Underlays for Pitched Roofs

British Board of Agrément Certificate:

BBA 07/4432 Pro clima Solitex Vapour permeable roofing underlay

Importing Agents: Ecological Building Systems See P14/509K

Applications: pitched roof underlay

unsupported rafter to rafter tiled or slated

fully supported with timber sheathing or rigid insulation board, tiled or slated or metal panel

warm ventilated and non-ventilated tiled or slated pitched roofs

cold ventilated and non-ventilated tiled or slated pitched roofs.

Materials:

Roof tile underlay without reinforcement.

Outer layers: spunbonded polypropylene felt fabric

central layer: monolithic nonporous TEEE (thermoplastic ether ester elastomer) membrane

Manufacturing process: bonding together through an extrusion-coating process.

Performance:

roof tile underlay prevents the ingress of windblown rain, dust and snow,

facilitate the control of surface and interstitial condensation in insulated roofs.

Properties:

Protects the building from the elements during construction

sd value: < 0.15 MNs/g increased protection to the entire structure.

Fire Rating E to [_______]

Roll size: 1800 mm. x 50 m.

Weight: 140 g/m2

Colour: Light brown/Grey text

Environmental Credentials:

Country of origin and manufacture: Germany,

Attributes:

Diffusion Open product for use in breathing construction,

Site issues:

Can be exposed to the elements for 6 months.

It must only be fitted using staples or tacks in areas protected by an overlap.

To maximise the wind-tightness if the external membrane it is imperative that all taping and attachment is done with utmost care.

Ensure detailed planning, particularly of fitting at the eaves and gables,

Ensure careful execution when fitting insulation over rafters.

Use with cable and pipe grommets P14/340A – 344A

Small damage repairs: Pro clima Tescon No. 1 P14/332A

Services apertures: Pipe Grommet: Pro clima Roflex to P14/343A or P14/344A

Delay between taping/sealing and air testing: Generally: 10 minutes minimum.

317A	WIND TIGHT, VAPOUR PERMEABLE, PITCHED ROOF UNDERLAY:

System: Complete vapour permeable wind-tightness system with all necessary adhesive agents.

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Reference: Pro clima Solitex Plus

Accreditation: CE Mark in accordance with DIN EN 13984

British Board of Agrément Certificate: BBA 07/4432 Pro clima Solitex Vapour permeable roofing underlay

Irish Agrément Certificate:

IBA 02/0138 Solitex Plus & Solitex UD Vapour Permeable Roofing Underlays for Pitched Roofs

NSAI Agrément Certificate: NSAI 07/0297

3rd party product endorsement: NHBC Standards 2007

Importing Agents: Ecological Building Systems See P14/509K

Product page: http://www.greenspec.co.uk/html/product-pages/solitex_plus.php

Applications:

External only

unsupported and supported tiled or slated pitched roof underlay

warm ventilated and non-ventilated tiled or slated pitched roofs

cold ventilated and non-ventilated tiled or slated pitched roofs.

Materials: 4 layers

Roof tile underlay with net reinforcement.

Outer layers: spun bonded polypropylene felt fabric

central layer: monolithic nonporous TEEE (thermoplastic ether ester elastomer) membrane

reinforcement net: Polypropylene

Manufacturing process: bonding together through an extrusion-coating process, using a combination of heat and pressure in a continuous process.

Performance:

provides a barrier to minimise the effects of wind load generated under wind gusts acting on slates and tiles when installed in accordance with this Certificate.

facilitate the control of surface and interstitial condensation in insulated roofs.

roof tile underlay offers resistance to tearing during installation and will give higher flexibility at low ambient temperatures.

Properties:

sd value: 0.03m or < than 0.15MNs/g See table in BBA Certificate.

Water vapour resistance: < 0.15 MNs/g

Nail tear resistance: > 350 N/m

Waterproof: > 2500 mm. of water column, waterproof when subjected to heavy rain.

Wind driven pelting rain: extreme resistance

Temperature range: -40 degrees C to +100 degrees C

Weight: 170 g/m2

Fire Rating E

Standard: Exceeds Type 1F reinforced bitumen underlay to BS 747

Roll size: 1500 mm. x 50 m. (smaller rolls available for window and floor connections)

Colour: Mid Blue & Dark blue text stripe/Dark grey & white grid back

Environmental Credentials:

Country of origin and manufacture: Germany,

Attributes:

Diffusion Open product for use in air impermeable moisture breathing construction,

Site issues:

Can be exposed to the elements for 6 months.

It must only be fitted using staples or tacks in areas protected by an overlap.

To maximise the wind-tightness of the external membrane it is imperative that all taping and attachment is done with utmost care.

Ensure detailed planning, particularly of fitting at the eaves and gables,

Ensure careful execution when fitting insulation over rafters.

Small damage repairs: Pro clima Tescon No. 1: to P14/332A

Services apertures: Pipe Grommet: Pro clima Roflex to P14/343A or P14/344A

Delay between taping/sealing and air testing: Generally: 10 minutes minimum.

318A	WINDTIGHT & WATER RESISTANT RAIN SCREEN WALLING MEMBRANE:

System: Complete vapour permeable wind resistant system with all necessary adhesive agents.

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Reference: Pro clima Solitex WA

Accreditation: CE Mark in accordance with DIN EN 13984

Irish Agrément Certificate:

IAB 04/0210 Solitex WA Breathable Wall Protection membrane

NSAI Agrément Certificate: NSAI 07/0297

Importing Agents: Ecological Building Systems See P14/509K

Applications:

External only

Behind rainscreen cladding

Materials: 100% Polypropylene microfiber fleece

Performance:

Protects building and thermal insulation from wind driven rain during construction

Protects building structure under the façade against wind and damp

Black (choice) so can be unseen through gaps in façade

Properties:

Protects the building from the elements during construction

sd value: < 0.05 m.

Moisture vapour resistance: < 0.038 MNs/g

Nail tear resistance: > 180 N

Temperature range: -40 degrees C to +100 degrees C

Weight: 100 g/m2

Fire Rating E

Roll size: 1500 mm. and 3000 mm. x 50 m. & 100 m.

Colour:

Black so unseen through gaps in façade

Other colours available

Environmental Credentials:

Country of origin and manufacture: Germany,

Attributes:

Diffusion Open product for use in breathing construction,

Site issues:

Can be exposed to the elements for 6 months.

It must only be fitted using staples or tacks in areas protected by an overlap.

It is not possible to perform quality control testing either using a pressure differential method such as using the Pro clima Wincon see P14/690 or by means of a visual test, such as the Blower Door See P14/910 & 970

It is therefore imperative that all taping and attachment is done with utmost care.

Ensure detailed planning, particularly of fitting at the eaves and gables,

Ensure careful execution when fitting insulation over rafters.

Accessories:

Adhesive tapes:

Pro clima Tescon No. 1 to P14/332A

Pro clima Tescon Profil to P14/336A

Pro clima Duplex to P14/355A

Small damage repairs: Pro clima Tescon No. 1: to P14/332A

Services apertures: Pipe Grommet: Pro clima Roflex to P14/343A or P14/344A

Delay between taping/sealing and air testing: Generally: 10 minutes minimum.

320A	GUN APPLIED NATURAL JOINT ADHESIVE:

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Product Reference: Eco Coll

Importing Agents: Ecological Building Systems See P14/509K

Product Page: http://www.greenspec.co.uk/html/product-pages/eco_coll.php

Adhesive: cartridge for use with standard applicator gun,

Material: Natural latex adhesive, casein, talc, cellulose, water and tree resin,

3rd party accreditation:

NSAI Agrément Certificate: NSAI 07/0297

Life expectancy: 60 years+

Temperature resistance: -10 to +40 degrees C.

Use with: Pro clima DB+ to P14/311A

Do not use with Pro clima Intello Plus to P14/310A

Use:

Natural adhesive for use with natural sheet to make a natural membrane

Internal applications only

For joints between membrane at laps

For joints between membrane and adjacent construction

Backgrounds: smooth masonry, plastered, rough surfaces or rough structural components

Application: 5 mm. thick bead,

Cartridge: 310 ml. sufficient for 5-10 meters,

Adhesive remover: water based solution

Product Reference: Glumex

Rough surfaces: increase bead size as necessary.

Delay between sealing and air testing: 12 to 24 hours depending on weather conditions

322A	GUN APPLIED ADHESIVE TO POROUS STRUCTURAL SURFACES:

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Product Reference: Orcon F

Importing Agents: Ecological Building Systems See P14/509K

Adhesive: tubular film sleeve or cartridge for use with standard applicator gun,

Material:

Non-ageing Acrylate polymers without softeners or halogenated compounds which is insusceptible to embrittlement.

Contains denatured alcohol (15%) allowing it to penetrate deep into stone substrates, ensuring a very tight bond.

Properties:

Exceptionally high inner strength (cohesion) while also being elastic.

Outstanding adhesion to building materials gives the joint the necessary safety and longevity.

High strength on building material substrates

Greater resistance to high humidity on building sites

Long lasting adhesion and elasticity

Frost resistant: to -20° C

Temperature range: -20° C to +80° C

Low VOC: compliant with Sentinel House Institute German indoor Air Quality standard

Life expectancy: 60+ years

Airtight bonding to DIN 4108-7, SIA 180 and ONorm B8110-2

3rd party accreditation:

NSAI Agrément Certificate: NSAI 07/0297

Applications:

Internal and external

Airtight outdoor joints e.g. vapour check for external roof insulation

Airtight outdoor joints e.g. sub or top vapour check for refurbishment reroofing

Wind proof bonding of roof underlay

Wind proof bonding of façade membranes

Use with:

Pro clima Intello Plus to P14/310A

Pro clima DB+ to P14/311A

all of Pro clima’s vapour checks, air-tightness and wind-tightness membranes,

PE Polyethylene

PA Polyamide (Nylon)

PP polypropylene

aluminium foils

Product Page: http://www.greenspec.co.uk/html/product-pages/orconf.php

Use: Multipurpose joint adhesive

Suitable for bonding to following:

To smooth, rough or stony surfaces, to concrete, plaster, render, lime based mineral plasters.

Do not use on:

unstable or crumbling surface unless grounded and stabilised See P14/580B

unprotected metal surfaces.

Rust resistant metals: See Pro clima Duplex to P14/355A

Preparation:

Damp surfaces: allow to dry

Grounding and stabilising: to P14/580

Packaging: tubular film sleeve or cartridge for use with standard applicator gun,

Application rate:

310 ml (g) cartridge approx. 5-10 m.

600 ml refill tube for approx. 10-25 m.

Application:

Internal and external applications

smooth surfaces: 5 mm. thick continuous bead

Mineral or rough structural component surfaces: increase bead size as necessary.

Following trades: Does not require a pressure batten.

Delay between sealing and air testing: 12 to 24 hours depending on weather conditions

330A	AIRTIGHTNESS LAP JOINT UNIVERSAL ADHESIVE TAPE:

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Product Reference: Uni Tape,

Importing Agents: Ecological Building Systems See P14/509K

Product Page: http://www.greenspec.co.uk/html/product-pages/unitape.php

Irish Agrément Certificate: IAB 07/0297 Pro clima intelligent airtight system (endorsed by NSAI)

Type: Single sided adhesive tape with quick release paper

Material: Acrylate which is free from solvents and softeners

Colour: pale blue

Size: 60 mm. wide x 30 m.

Properties:

Tears off easily

Permeable universal tape

Temperature resistance: -40 to +90 degrees C.

Life expectancy: 60+ years

Airtight bonding to DIN 4108-7, SIA 180 and ONorm B8110-2

Use with:

Pro clima Intello Plus to P14/310A

Pro clima DB+ to P14/311A

Application:

Internal use only

Membrane lap joints See P14/600 & 625

Bonds overlaps between sheets of vapour check

Joints to adjacent structural components See P14/610 & 620

Gable walls are treated similarly.  .

Applied to large patch repairs to P14/682

Suitable backgrounds:

joints to smooth, non-mineral structural components

E.g. jamb wall made of OSB panels See work section G20

Sheathing paper membranes

Foil membranes

Tools: pressure sealing to P14/390A

Delay between taping/sealing and air testing: Generally: 10 minutes minimum.

331A	HOLE REPAIR ADHESIVE TAPE:

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Product Reference: Uni Tape XL,

Importing Agents: Ecological Building Systems See P14/509K

Type: Single sided adhesive tape with release paper

Colour: pale blue

Size: 150 or 200 mm. wide x 15 or 30 m.

Material: Backing: special reinforced paper

Use with:

Pro clima Intello Plus to P14/310A

Pro clima DB+ to P14/311A

Uni Tape patch to P14/350A

Application:

Internal use only

Sealing internal insulation injection hole patches indoors, See P14/350A & P14/685

Sealing damage repairs

Delay between taping/sealing and air testing: Generally: 10 minutes minimum.

331B	HOLE REPAIR ADHESIVE TAPE:

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Product Reference: Uni Tape XL easy

TAPE XL easy: pre-cut patches

Importing Agents: Ecological Building Systems See P14/509K

Use with:

Pro clima Intello Plus to P14/310A

Pro clima DB+ to P14/311A

Uni Tape Patch to P14/350A

Single sided adhesive tape with release paper

Colour: pale blue

Size: 150 or 200 mm. wide x 15 or 30 m.

Material: Backing: special reinforced paper

Application:

Internal use only

Sealing internal insulation injection hole patches indoors, See P14/350A & P14/685

Sealing damage repairs

Delay between taping/sealing and air testing: Generally: 10 minutes minimum.

332A	MEMBRANE OVERLAP FLEXIBLE AIRTIGHTNESS UNIVERSAL SEALING ADHESIVE TAPE:

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Product Reference: Tescon No. 1

Importing Agents: Ecological Building Systems See P14/509K

3rd party accreditation:

NSAI Agrément Certificate: NSAI 07/0297

Type: Single sided, flexible, multipurpose adhesive tape with 1 release paper

Colour: dark blue

Size: 60 mm. wide x  30 m.

Properties:

Tears off easily by hand

High flexibility

High elasticity: resistant to piercing in corners

Life expectancy: 60+ years

Temperature resistance: -40 to +90 degrees C

Airtight bonding to DIN 4108-7, SIA 180 and ONorm B8110-2

Materials:

Backing: perforated Polyethylene PE-foil and adhesive

Acrylate which is free from solvents and softeners

Use with:

Pro clima Intello Plus to P14/310A

Pro clima DB+ to P14/311A

Pro clima Solitex Plus to P14/317A

Suitable backgrounds:

Wood based panels: OSB, MDF

Wood fibre softboard: e.g. Gutex,

Application: Multi-purpose,

Internal and external use

Wood based boards: sealing butt joints

Membrane lap joints See P14/600 & 625

damage repairs See P14/331A

Seals around service penetrations, e.g. around pipes See P14/340A - P14/345A

Insulation injection hole repairs See P14/350A

Product Page: http://www.greenspec.co.uk/html/product-pages/unitape.php

Delay between taping/sealing and air testing: Generally: 10 minutes minimum.

332B	MEMBRANE OVERLAP FLEXIBLE AIRTIGHTNESS UNIVERSAL SEALING ADHESIVE TAPE:

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Product Reference: Tescon Vana

Importing Agents: Ecological Building Systems See P14/509K

3rd party accreditation:

NSAI Agrément Certificate: NSAI 07/0297

Single sided, flexible, multipurpose adhesive tape with 1 release paper

Colour: dark blue

Size: 60 mm. wide x  30 m.

Properties:

High tensile strength

Tears off easily by hand

High flexibility

Life expectancy: 60+ years

Temperature resistance: -40 to +90 degrees C

Airtight bonding to DIN 4108-7, SIA 180 and ONorm B8110-2

Materials:

Backing: perforated Polyethylene PE-foil and adhesive

Acrylate which is free from solvents and softeners

Use with:

Pro clima Intello Plus to P14/310A

Pro clima DB+ to P14/311A

Pro clima Solitex Plus to P14/317A

Suitable backgrounds:

Wood based panels: OSB, MDF

Wood fibre softboard: e.g. Gutex, with Pro clima Tescon Primer RP to P14/370B

Application: Multi-purpose,

Internal and external use

Wood based boards: sealing butt joints

Membrane lap joints See P14/600 & 625

damage repairs See P14/331A

Seals around service penetrations, e.g. around pipes See P14/340A - P14/345A

Insulation injection hole repairs See P14/350A

Delay between taping/sealing and air testing: Generally: 10 minutes minimum.

333A	AIRTIGHTNESS ADHESIVE TAPE:

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Product Reference: Rapid Cell

Importing Agents: Ecological Building Systems See P14/509K

Single sided adhesive tape with no release paper for rapid application, waxed backing,

Colour: Green

Size: 50 mm. wide x 30 m.

Use with:

Pro clima Intello Plus to P14/310A

Pro clima DB+ to P14/311A

Advantages:

Time saving in comparison to tapes with release paper: approx.  60%

Tears off easily

Disadvantages:

Won’t stick to itself

Application: rapid application,

Membrane lap joints See P14/600 & 625

Bonds membrane to wood based panel (e.g. OSB) See work section G20

Bonds joints between wood based panels (e.g. OSB) See work section G20

Delay between taping/sealing and air testing: Generally: 10 minutes minimum.

334A	PLASTERED WALL ABUTMENT AIRTIGHTNESS JOINT ADHESIVE TAPE:

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Product Reference: Contega PV

Importing Agents: Ecological Building Systems See P14/509K

3rd party accreditation:

NSAI Agrément Certificate: NSAI 07/0297

Preceding trade: plaster undercoat to receive tape See work section M20.

Type: Single sided airtight fleece with plaster reinforcement mesh

Purpose: for secure, long-lasting joints between membrane and plastered surfaces

Materials:

3 layers PET fleece

plaster reinforcement mesh: latex-reinforced

Acrylate adhesive, free from solvents and softeners

Colour: pale blue fleece and dark blue plaster reinforcement mesh

Properties:

Life expectancy: 60 years +

Temperature resistance: -40 to +90 degrees C

Application:

Internal use only

high quality bond

Suitable backgrounds:

wood based panel (e.g. OSB), See work section G20

plastered masonry See work sections F10 or F30 & M20

Size: 200 mm. wide x 15 m.

The airtight bond is completed once the fleece is plastered into place.

The latex reinforced layer increases the strength of the adjoining plasterwork.

Use with:

Pro clima Intello Plus to P14/310A

Pro clima DB+ to P14/311A

Delay between taping/sealing and air testing: Generally: 10 minutes minimum.

Completion: others to apply plaster onto fleece and push through, See work section M20.

335A	MEMBRANE PERIMETER BONDING TO METAL, AIRTIGHTNESS SEALING ADHESIVE TAPE:

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Product Reference: Duplex

Importing Agents: Ecological Building Systems See P14/509K

3rd party accreditation:

NSAI Agrément Certificate: NSAI 07/0297

Type: Double sided adhesive tape with release paper

Materials: Acrylate which is free from solvents and softeners

Application:

Internal and external uses

bond to metal framing in dry construction

membrane to membrane overlaps

rust resistant metals

Properties:

Air tight and moisture proof

Rain-proof

Temperature resistance: -40 to +90 degrees C.

Colour: white with blue reinforcing mesh

Size: 25 mm. wide x 20 m.

Use with:

Pro clima Intello Plus to P14/310A

Airtightness membrane: Pro clima DB+ to P14/311A

Wind tight rain proof membrane: Pro clima Solitex Plus, to P14/317A

PE Polyethylene vapour barriers to metal studs

PA Polyamide (Nylon) vapour barriers to metal studs

PP polypropylene vapour barriers to metal studs

aluminium foils vapour barriers to metal studs

Tools:

Tape dispenser: to P14/391A

Pressure applicator: to P14/390A

Delay between taping/sealing and air testing: Generally: 10 minutes minimum.

336A	CORNER AIRTIGHTNESS SEALING ADHESIVE TAPE:

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Product Reference: Tescon Profil

Importing Agents: Ecological Building Systems See P14/509K

Product Page: http://www.greenspec.co.uk/html/product-pages/tescon_profile.php

3rd party accreditation:

NSAI Agrément Certificate: NSAI 07/0297

Type: Single sided, flexible, multi-purpose adhesive tape with 3-part release paper

Application:

Internal and external

for quick and awkward tight corners at perimeter of windows doors and rooflights

Colour: dark blue

Size: 60 mm. wide x 30 m.

Properties:

Tears off easily by hand

High flexibility

High elasticity: resistant to piercing in corners

Release papers separate easily

Life expectancy: 60+ years

Temperature resistance: -40 to +90 degrees C

Airtight bonding to DIN 4108-7, SIA 180 and ONorm B8110-2

Materials:

Backing: perforated Polyethylene PE-foil and adhesive

Acrylate which is free from solvents and softeners

Use with:

Pro clima Intello Plus to P14/310A

Pro clima DB+ to P14/311A

Pro clima Solitex Plus to P14/317A

Application:

Internal and external corner joints, sealing reveals,

Abutments with windows,

Abutments with roof windows,

Abutments with doors,

Abutments with planed timber.

It is equipped with three strips of release paper.

This allows ‘activation’ of a single part of the adhesive surface and sealing of one side at a time.

In the second step, remove the remainder of the release paper and finish the sealing of the joint.

Tools: Pressure applicator: to P14/390A

Delay between taping/sealing and air testing: Generally: 10 minutes minimum.

337A	AIRTIGHTNESS SEALING ADHESIVE TAPE FOR WINDOW JOINTS TO PLASTERED MASONRY:

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Product Reference: Contega FC

Importing Agents: Ecological Building Systems See P14/509K

Product Page: http://www.greenspec.co.uk/html/product-pages/contega.php

3rd party accreditation:

NSAI Agrément Certificate: NSAI 07/0297

Type: Single sided, flexible, adhesive tape

Materials:

3 layer PET fleece

Adhesives: integrated non-aging acrylate, free from solvents and softeners

Colour: pale blue fleece

Properties:

High temperature resistance

Strong durable bond

Gypsum plaster compatible

Airtight

Vapour resistant: > 11.5 MNs/G

Sd value: 2.3 m.

Temperature resistant: long term -40 to +90 degrees C

Working temperature from -10 degrees C

Quality & testing requirements: ensure window joints are RAL German quality assurance association compliant.

(airtight on the inside, higher diffusion resistance on the inside than the outside)

Size: 85 mm. wide x 15 m.

Applications: high quality bond

Internal use only

airtight internal transition from adjoining masonry brickwork, blockwork or concrete:

corners at perimeter of window frame

corners at perimeter of door frame

corners at perimeter of rooflights

visible rafters

visible roof beams

for bedding into bonding plaster

plastered masonry See work sections F10 or F30 & M20

Purpose: for secure, long-lasting joints between:

membrane, structural and secondary elements and plastered surfaces

Completion: others to apply plaster onto fleece, See work section M20.

Delay between taping/sealing and air testing: Generally: 10 minutes minimum.

337B	AIRTIGHTNESS SEALING ADHESIVE TAPE FOR WINDOW JOINTS TO PLASTERED MASONRY:

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Product Reference: Contega SL

Importing Agents: Ecological Building Systems See P14/509K

Type: Single sided, flexible, adhesive tape

Materials:

2 layer PET fleece

Adhesives: integrated non-aging Acrylate, free from solvents and softeners

Colour: pale blue fleece

Properties:

High flexibility

High temperature resistance

Strong durable bond

Gypsum plaster compatible

Airtight

Vapour resistant: > 11.5 MNs/G

Sd value: 2.3 m.

Temperature resistant: long term -40 to +90 degrees C

Working temperature from -10 degrees C

Quality & testing requirements: ensure window joints are RAL German quality assurance association compliant.

(airtight on the inside, higher diffusion resistance on the inside than the outside)

Size: 85 mm. and 120 mm. wide x 30 m.

Applications: high quality bond

Internal use only

airtight internal transition from adjoining masonry brickwork, blockwork or concrete:

corners at perimeter of window frame

corners at perimeter of door frame

corners at perimeter of rooflights

visible rafters

visible roof beams

for bedding into bonding plaster

plastered masonry See work sections F10 or F30 & M20

use Orcon F to P14/322A to adhere Contega SL to P14/337B to bricks or blocks; or plaster may be applied directly on top of the fleece

Purpose: for secure, long-lasting joints between:

membrane, structural and secondary elements and plastered surfaces

Completion: others to apply plaster onto fleece, See work section M20.

Delay between taping/sealing and air testing: Generally: 10 minutes minimum.

340A	SERVICE APERTURE AIRTIGHT SINGLE CABLE GROMMET:

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Product Reference: Kaflex Mono Grommet

Importing Agents: Ecological Building Systems See P14/509K

Product Page: http://www.greenspec.co.uk/html/product-pages/karflex.php

3rd party accreditation:

NSAI Agrément Certificate: NSAI 07/0297

Application: internal only

Performance:

Life expectancy: 60 years +

Temperature resistance: -40 to +100 degrees C

Properties:

Airtight seal to service passing through

High elasticity and high protection against piercing

Can accommodate services being moved through grommet once installed without loss of seal

Material:

non-ageing elastic EPDM

integrated Acrylate solvent-free adhesive tape

release paper for ease of application

Use with:

Pro clima Intello Plus to P14/310A

Pro clima DB+ to P14/311A

Size: 145 x 145 mm.

Aperture size range: 6 mm. to 12 mm.

Apertures: single

Service type: pipes or small cables,

Delay between taping/sealing and air testing: Generally: 10 minutes minimum.

341A	SERVICE APERTURE AIRTIGHT DOUBLE CABLE GROMMET:

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Product Reference: Kaflex Duo Grommet

Importing Agents: Ecological Building Systems See P14/509K

Product Page: http://www.greenspec.co.uk/html/product-pages/karflex.php

3rd party accreditation:

NSAI Agrément Certificate: NSAI 07/0297

Application: internal only

Performance:

Life expectancy: 60 years +

Temperature resistance: -40 to +100 degrees C

Properties:

Airtight seal to service passing through

High elasticity and high protection against piercing

Can accommodate services being moved through grommet once installed without loss of seal

Material:

non-ageing elastic EPDM

integrated Acrylate solvent-free adhesive tape

release paper for ease of application

Use with:

Pro clima Intello Plus to P14/310A

Pro clima DB+ to P14/311A

Size: 145 x 145 mm.

Aperture size range: 6 mm. to 12 mm.

Apertures: double

Service type: pipes or small cables,

Delay between taping/sealing and air testing: Generally: 10 minutes minimum.

342A	SERVICE APERTURE AIRTIGHT MULTIPLE CABLE GROMMET:

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Product Reference: Kaflex Multiple Grommet

Importing Agents: Ecological Building Systems See P14/509K

Product Page: http://www.greenspec.co.uk/html/product-pages/karflex.php

3rd party accreditation:

NSAI Agrément Certificate: NSAI 07/0297

Application: internal only

Performance:

Life expectancy: 60 years +

Temperature resistance: -40 to +100 degrees C

Properties:

Airtight seal to service passing through

High elasticity and high protection against piercing

Can accommodate services being moved through grommet once installed without loss of seal

Material:

non-ageing elastic EPDM

integrated Acrylate solvent-free adhesive tape

release paper for ease of application

Use with:

Pro clima Intello Plus to P14/310A

Pro clima DB+ to P14/311A

Size: 140 x 140 mm.

Aperture size range: 6 mm. to 12 mm.

Apertures: single

Service type: pipes or small cables,

Apertures: set out for multiple apertures, up to 16 services, arrangement: to suit services,

Cutting apertures: Using puncher tool: to P14/393A

Delay between taping/sealing and air testing: Generally: 10 minutes minimum.

343A	SERVICE APERTURE AIRTIGHT PIPE GROMMET:

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Product Reference: Roflex 20 Grommet

Importing Agents: Ecological Building Systems See P14/509K

Product Page: http://www.greenspec.co.uk/html/product-pages/Roflex.php

3rd party accreditation:

NSAI Agrément Certificate: NSAI 07/0297

Application: internal and external

Performance:

Life expectancy: 60 years +

Temperature resistance: -40 to +120 degrees C

Properties:

Airtight seal to pipework passing through

High elasticity and high protection against piercing

Can accommodate pipe(s) being moved through grommet once installed without loss of seal

Material:

non-ageing elastic EPDM

Use with:

Pro clima Intello Plus to P14/310A

Size: 145 x 145 mm.

Aperture size range: 6 mm. to 12 mm.

Pipe aperture size range: 15 mm. to 30 mm.

Apertures: single

Service type: pipes ,

Sealing to membrane: Adhesive tape: Tescon No. 1 see P14/332A.

Delay between taping/sealing and air testing: Generally: 10 minutes minimum.

344A	SERVICE APERTURE AIRTIGHT PIPE GROMMET:

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Product Reference: [Roflex 50, 100, 150 & 200 Grommet]

Importing Agents: Ecological Building Systems See P14/509K

Product Page: http://www.greenspec.co.uk/html/product-pages/Roflex.php

3rd party accreditation:

NSAI Agrément Certificate: NSAI 07/0297

Application: internal and external

Performance:

Life expectancy: 60 years +

Temperature resistance: -40 to +120 degrees C

Properties:

Airtight seal to pipework passing through

High elasticity and high protection against piercing

Can accommodate pipe(s) being moved through grommet once installed without loss of seal

Material:

non-ageing elastic EPDM

Use with:

Pro clima Intello Plus to P14/310A

Size: see schedule

Pipe aperture size range: see schedule.

Apertures: single

Service type: pipes ,

Schedule:

Reference	pipe size range	Grommet size[

Roflex 50		50 to 90 mm.	140 x 140 mm.

Roflex 100	100 to 120 mm.	200 x 200 mm.

Roflex 150	120 to 170 mm.	250 x 250 mm.

Roflex 200	170 to 220 mm.	300 x 300 mm.]

Sealing to membrane: Adhesive tape: Tescon No. 1 see P14/332A.

Delay between taping/sealing and air testing: Generally: 10 minutes minimum.

345A	SERVICE APERTURE AIRTIGHT PIPE SEAL USING TAPE:

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Product Reference: Tescon No. 1 See P14/332A.

Importing Agents: Ecological Building Systems See P14/509K

Product Page: http://www.greenspec.co.uk/html/product-pages/tescon_1.php

Size: cut to short lengths, to reduce risk of stretching tape at installation.

Tools: Pressfix: to P14/390A

Delay between taping/sealing and air testing: Generally: 10 minutes minimum.

350A	INSULATION INJECTION HOLE REPAIR PATCH:

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Product Reference: Uni Tape Patch

Importing Agents: Ecological Building Systems See P14/509K

Pre-cut patches

Size: 180 x 180 mm.

Application: for repairing internal:

insulation injection holes in membrane See P14/685

large perforations or damage

Sealing: repair tape: to P14/331A

Uni tape to P14/330A

Delay between taping/sealing and air testing: Generally: 10 minutes minimum.

370B	PRIMER/STABILISER

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Product Reference: Tescon Primer RP.

Importing Agents: Ecological Building Systems See P14/509K

Applications: Floors, Roofs, Walls, structure,

Suitable backgrounds:

Plastered surfaces

Wood fibreboard surfaces

Woodfibreboard softboard to P10/___ e.g. Gutex

Wood

Blockwork walls

Concrete

Sand cement screed

Plaster skimmed surfaces

Use with and prepare surface for:

Adhesives:

Ecological and good indoor air quality Pro clima Eco Coll to P14/320A

Pro clima Orcon F to P14/322A

Adhesive tapes:

Pro clima Tescon No. 1 to P14/332A

Pro clima Tescon Vana to P14/332B

Pro clima Tescon Profil to P14/336A

Material: Solvent-free Acrylate copolymer primer

Dissolvent: water

Properties:

Working temperature: +2 to +45 degrees C

Temperature resistance: -40 to +90 degrees C

Storage: frost protection, frost-free, shelf life 24 months

Contents: 0.75, 1 or 2.5 litres

Coverage: 7.5 m2, 10 m2 or 25 m2

Mixing: shape bottle before application,

Preparation: surfaces shall be:

Free from dust, loose materials, or sawdust

Smooth, dry and stable

Surfaces may be wet, bond will still be achievable

Thawed and not frozen

Surfaces must be set and fully cured and dried

Application: to P14/580A

For speedy application: no drying of primer is necessary

Bonding of Tescon No.1 to P14/332A or Tescon Vana to P14/332B to wet primer is possible

Use with wind tightness underlay membranes:

Pro clima Solitex Plus: to P14/317A

Pro clima Intello Plus to P14/310A

380	AIRTIGHT & PRE-INSULATED ATTIC ACCESS HATCH/LADDER

Manufacturer: Wellhofer, See P14/509K

Product Reference: Wellhofer attic hatch

UK & Ireland Agent: Ecological Building Systems UK Ltd.  See P14/509K

Manufactured and engineered in Germany

Airtightness test: DIN [_____]

Insulation test: DIN [_____]

Accreditation: CE Mark in accordance with DIN [_____]

Airtight seal on door is maintained by means of a pre-stressed spring which ensures the door remains airtight, even when a blower door test is carried out.

Seal between door and hatch frame: rubber gasket.

Durability of rubber gasket: tested [________]

Seal between frame and ceiling: Airtight sealing system, no air leakage occurs.

Seal to surround: double sided adhesive tape and Insulation strip.

Delay between taping/sealing and air testing:

Generally: 10 minutes minimum

Orcon F: to P14/322A or Eco Coll: to P14/320A: 12 to 24 hours depending on weather conditions

Includes a pre-insulated hatch door.

Size of ceiling opening: (Other sizes are available)

Length: 1200 mm.

Width: 600 mm.

Height: 250 mm.

Size of the casing is 15 mm. smaller in length and width than the ceiling.

Optional extras:

Attic ladders are available on request.

381A	AIRTIGHT BOX FOR HOUSING FLUSH MOUNTED CEILING DOWN-LIGHT LUMINAIRE:

Manufacturer: Optime, See P14/509K

Product Reference: OPTIME Downlight protector Mini

UK & Ireland Agent: Ecological Building Systems UK Ltd.  See P14/509K

Accreditation: CE Mark in accordance with DIN [_____]

3rd party accreditation: [____________]

3rd party endorsement: Recognised by Nemko.

Background: timber joisted plasterboard ceiling: to work section K10

Size: 200 x 200 x 140 mm.

Materials: recyclable [____]

One stop solution safe easy to install sealing system for downlights.

Reduce heat loss, condensation risk, energy consumption and CO2 footprint.

Improve comfort,

Manufactured and engineered in Germany

Airtightness: [_____]

Airtightness test: DIN [_____]

Ensures an effective moisture barrier is maintained.

Thermal insulation: [_______]

Insulation test: DIN [___]

Fire performance:

Flammability: non-flammable, will tolerate high temperatures in accordance with building regulations.

Fire resistance: None

Do not include a transformer with luminaire (size of the box causes too high a temperature for the transformer).

Luminaire wattage:

Optimum: low energy luminaires

Maximum: 50 W

Simple to install.

It is essential that light fittings are installed as per the Optime fitting manual, contact us for further information.

Supplied with a ‘snap on’ airtight cover for housing the light fixing tightly.

Cover is simple to fit and requires no additional tools.

Application: all types of roofs and ceilings

381B	AIRTIGHT BOX FOR HOUSING FLUSH MOUNTED CEILING DOWN-LIGHT LUMINAIRE & TRANSFORMER:

Manufacturer: Optime, See P14/509K

Product Reference: OPTIME Downlight protector Maxi.

UK & Ireland Agent: Ecological Building Systems UK Ltd.  See P14/509K

Accreditation: CE Mark in accordance with DIN [_____]

3rd party accreditation: [____________]

3rd party endorsement: Recognised by Nemko.

Background: timber joisted plasterboard ceiling: to work section K10

Size: 320 x 320 x 160

Simple to install.

One stop solution safe easy to install sealing system for downlights.

Reduce heat loss, condensation risk, energy consumption and CO2 footprint.

Improve comfort,

Manufactured and engineered in Germany

Airtightness: [_____]

Airtightness test: DIN [_____]

Ensures an effective moisture barrier is maintained.

Thermal insulation: [_______]

Insulation test: DIN [___]

Fire performance:

Flammability: non-flammable, will tolerate high temperatures in accordance with building regulations.

Fire resistance: None

Will accommodate a transformer with the luminaire

Luminaire wattage:

Optimum: low energy luminaires

Maximum: 50 W

Materials: recyclable [____.

It is essential that light fittings are installed as per the Optime fitting manual, contact us for further information.

Supplied with a ‘snap on’ airtight cover for housing the light fixing tightly.

Cover is simple to fit and requires no additional tools.

Application: all types of roofs and ceilings

Optional extras:

Available with a flexible mounting between joists.

381C	AIRTIGHT BOX FOR HOUSING FLUSH MOUNTED LOFT CEILING DOWN-LIGHT LUMINAIRE:

Manufacturer: Aico, See P14/509K

T	0870 758 4000

E	Enquiries@aico.co.uk	W	www.aico.co.uk

Product Reference: Loftcap ALC274

W	http://www.aico.co.uk/Fire-Barriers.html

3rd party approvals: Lighting Association & NHBC

Size: 274 - 224 diameter x 162 mm.

Background: timber [roof joisted/trussed rafters], plasterboard ceiling: to work section K10

Material: inert mineral fibres and organic binders

One stop solution safe easy to install sealing system for down-lights.

Function:

Reduce: heat loss, condensation risk, energy consumption and CO2 footprint.

Improve comfort,

Airtightness: [_____]

Airtightness test: CIBSE TM23 [_____]

Ensures an effective moisture barrier is maintained.

Thermal insulation performance:_______]

Insulation test: [___]

Vapour performance: [____]

Acoustic performance: none

Non-electrically conductive - no risk of electric shock or fire hazard

Fire performance: non-combustible

Do not include a transformer with luminaire (size of the box causes too high a temperature for the transformer).

Luminaire wattage:

Optimum: low energy luminaires

Maximum: [__] W

Performance:

effective vapour seal

effective thermal seal

rigid enough to support loft insulation.

Will not cause the light fitting to overheat

Non-metallic and low risk of condensation water droplet formation

Cable entry:

piercing with a sharp instrument or pencil,

pass cabling through the cover, inside to out,

seal with sealant

Sealant type: [_______]

Fixing:

place over the downlight and seal with Sealant.  No screws or clips required

Sealant type: [_______]

Simple to install.

It is essential that light fittings are installed as per the Aico fitting manual, contact them for further information.

Application: all types of attic roofs and not intermediate floor ceilings.

Maintains sufficient air space around the light fitting in order to avoid overheating

Durable construction - rot, corrosion and vermin resistant

Maintenance free

Weight: 350 g can be carried on ceiling board

Fibres used are exonerated from classification according to HSE guidelines

Tested and approved by the Lighting Association

Ensure insulation is laid over the cap to ensure uninterrupted coverage of thermal insulation in loft spaces, ensuring minimal heat loss through the ceiling.

382A	FIRE RESISTANT AIRTIGHT BOX FOR HOUSING FLUSH MOUNTED CEILING DOWNLIGHT LUMINAIRE:

Fire resistance: [_______] Hours to BS 476:Part [_]

Manufacturer: [____]

Product Reference: [___]

383A	AIRTIGHT FLUSH MOUNTED 13 AMP SOCKET JUNCTION BOX:

Backgrounds:

Plasterboard dry lining: to work section K10

Masonry: to work section F10, chased to receive conduit and flush boxes

Fire resistance: 2 Hours to EN [_____]

Acoustic performance: suitable to include in walls of up to [__] dB

Airtightness: [_____]

Materials: plastics box body

Plug and go airtight cable connections

Airtight seal achieved by: perimeter rubber seal at back of face plate compressed by fastening device

Manufacturer: [____]

Product Reference: [___]

383B	AIRTIGHT ACOUSTIC & FIRE RESISTANT FLUSH MOUNTED 13 AMP SOCKET JUNCTION BOX INSERT:

Backgrounds:

Plasterboard dry lining: to work section K10

Masonry: to work section F10, chased to receive conduit and flush boxes

Fire resistance: 2 Hours to EN [_____]

Acoustic performance: suitable to include in walls of up to 67 dB

Airtightness: [_____]

Materials:

plastics or metal box body

Intumescent and acoustic socket box insert

Plug and go airtight cable connections

Airtight seal achieved by: perimeter rubber seal at back of face plate compressed by fastening device

Manufacturer: Astroflame,

T	0800 023 2482	T	01329 844500

E	sales@astroflame.com	W	www.astroflame.com

Product Reference: Intumescent and acoustic socket box insert

390A	TOOL: ADHESIVE/TAPE PRESSING AID:

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Product Reference: Pro clima Pressfix

Importing Agents: Ecological Building Systems See P14/509K

391A	DOUBLE SIDED TAPE DISPENSER:

For use with Pro clima Duplex: to P14/335A

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Product Reference: Pro clima Tape Dispenser

Importing Agents: Ecological Building Systems See P14/509K

392A	SEALANT GUN:

Single row sealant dispenser

Product Reference: dispensing gun

392B	SEALANT GUN: DOUBLE DISPENSING HEAD

Double row sealant dispenser

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Product Reference: Pro clima DKF double dispensing gun

Importing Agents: Ecological Building Systems See P14/509K

Application: to P14/110B.

Advantages: speed of application, one pass, keeps adhesive ‘open’ time longer.

393A	TOOL: APERTURE PUNCH:

For use with Pro clima Kaflex Multiple: to P14/342A to cut holes to suit project requirements

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Product Reference: Pro clima Puncher

Importing Agents: Ecological Building Systems See P14/509K

394A	TOOL: MEMBRANE STAPLER:

Type: pneumatic or electric stapler

Do not use hammer tapper type stapler

MATERIALS

410A	FASTENERS: STAPLES

Applications: [

Air-tightness layer

Roofing underlay

Rainscreen breather membrane]

Type: Staples

Material: [

Stainless steel

Galvanized mild steel]

Width: 10 mm. wide

Length: 8 mm.

Application: stapler: to P14/394A

Spacing:

Airtightness layer:

Generally: 100 - 150 mm.

Pro clima Intello plus: 50 - 100 mm.

Pro clima DB+: 100 - 150 mm.

With blow-in insulation systems: 50 - 100 mm. See work section P11

Roofing underlay:

Pro clima Solitex Plus: to P14/317A

See IAB Certificate application table.

The underlay should be tacked at the head of the sheet only,

Spacing: </= 1200 mm.

It is important that all tacking nails be covered by 100 mm. overlap of the next underlay course.

411A	FASTENERS: TACKS

Application: roofing underlay

Size: 3 mm. diameter x 20 mm. long

Type: extra large head felt nails

Material: copper, aluminium alloy, galvanized steel

The underlay should be tacked at the head of the sheet only, at centres not exceeding 1200 mm.

See IAB Certificate application table.

It is important that all tacking nails be covered by the overlap of the next underlay course so that the minimum head-lap is maintained between the tacks and the lower edge of the overlapping underlay.

420A	SOFTWOOD NOGGINS

Provision: to P14/565.

Application: within timber framing

Material: Reclaimed, locally grown or FSC temperate softwood

Moisture content: Seasoned to 20 % +/- 2%

Size: to suit

Purpose:

To provide support to laps in membranes otherwise unsupported by framing

To provide support for pressure & support battens

To protect from wind pressure buffeting and premature failure of membranes

Location: place at membrane overlaps between framing.

NB. It is not essential to provide support at all lap joints, an adequate joint can be achieved by ensuring the membrane is taught between supports, using the pressure application tool to ensure a good bond

Spacing: to ensure membranes are supported at maximum 600 mm. centres

Secure to structural timber adjacent to lap joints.

421A	PRESSURE BATTENS:

Material: Reclaimed, locally grown or FSC temperate softwood

Moisture content: Seasoned to 20 % +/- 2%

Size: 25 mm. x width to correspond to the backing structural timber

Purpose:

to provide mechanical retention and compression on lapped and sealed joints

to protect from wind pressure buffeting and premature failure.

Location: place at membrane overlaps.

Spacing: to ensure membranes are supported at maximum 600 mm. centres

422A	SUPPORT BATTENS:

Material: Reclaimed, locally grown or FSC temperate softwood

Moisture content: Seasoned to 20 % +/- 2%

Size: 25 x width to correspond to the backing structural timber

Purpose:

To provide support to heavy insulation which may exert pressure on the membrane

To provide support to blown-in insulation materials that may slump

Location:

Spacing: to ensure membranes are supported at maximum 500 mm. centres

Centres: To support weight of blown insulation against Pro clima Intello membrane: 500 mm.

423A	SERVICE ZONE BATTENS:

Material: Reclaimed, locally grown or FSC temperate softwood

Moisture content: Seasoned to 20 % +/- 2%

Size: 30 x 30 mm.

Purpose:

To provide support to internal lining boards

To provide space for service runs inside of the air-tightness membrane

To avoid potential penetration of airtightness layer by fasteners

Location: place on membrane overlaps.

Spacing: to ensure linings are supported at maximum 600 mm. centres

424A	TILING/SLATING BATTENS & COUNTER-BATTENS:

Purpose:

To secure underlay/wind-tightness membrane

To support roof tiling/slating

To provide drainage route to rainwater goods

See work section [H60 – H66]

FABRICATIONS

WORKMANSHIP

500A	UK CODE OF PRACTICE: install in accordance with: [

BS 5250, BS 5534-1, BS 5925, BS 8000-6.]

500B	NON-UK CODE OF PRACTICE: install in accordance with: [

German Standards: DIN 4108-2 and -7

Swiss Standards: SIA 180:01

Austrian Standards: ÖNorm B8110-2]

501	AGRÉMENT CERTIFICATE

Install in accordance with: [

Irish Agrément Certificate:

IAB 02/0138 Solitex Plus & Solitex UD Vapour Permeable Roofing Underlays for Pitched Roofs

IAB 07/0297 Pro clima intelligent airtight system (NSAI endorsed)

British Board of Agrément Certificate:

BBA 07/4432 Pro clima Solitex Vapour permeable roofing underlay]

502	MANUFACTURERS RECOMMENDATIONS:

Install in accordance with: manufacturer’s recommendations as described in: [

Pro clima Intelligent Airtight and Windtight building systems Product Portfolio (not dated, published 2009)

Pro clima INTELLO High performance intelligent vapour check Application Guide (vh_intello_11.07)

Pro clima System: Interior insulation - INTELLO11.2008]

503	CONFLICTS OR CONTRADICTIONS

505	TRAINING VIDEO: INSTALLATION FILM:

As part of tool box talks show video to site staff.

A new airtightness film “pro clima intelligent airtightness tapes and membranes”

Ecological Building Systems has recently developed an excellent film on intelligent airtight installation for specifiers and building professionals.

The film guides viewers through products within the pro clima intelligent airtight system and includes tapes such as Tescon No. 1; Orcon F glue; pipe and cable grommets along with pro clima's leading brand - Intello Plus an intelligent airtight vapour control membrane.

The film also guides installers step by step through correct installation and critical junctions to consider when building airtight construction.

The film is available to view freely on green building store's website:

www.greenbuildingstore.co.uk/page--pro-clima-airtightness-airtightness-film.html

508	TRAINING:

Ensure all applicators/installers have received suitable training from the manufacturer’s UK or Irish Agents:

On-site guidance is offered in England, Wales and Scotland by the UK Agent.  See P14/509K

“Upskilling for airtightness”

Off-site training is offered in Ireland by the Irish Agent at a training centre.  See P14/509K

508K	APPLICATORS/INSTALLERS:

Obtain installation/application sub-contract services from one company for each type of work unless specified or agreed otherwise in advance.

Ensure the company has had training in the use of the materials See P14/508 or

Organise the training for the project on or off-site.  See P14/508

Obtain from only one of the following trained/experienced applicators/installers:

APPLICATORS/INSTALLERS:

Contact Importing Agents Suppliers for the latest list of Applicator/installers

WALES:

Pen Y Coed Construction & Insulation Ltd.  Pen y Lan, Meifod, Powys, SY22 6DA

T	01938 500 797

E	info@penycoed-warmcel.com 	W	www.penycoed-warmcel.com

JPW Construction Ltd.  6 Vane Hall Place, Pentrerhedyn St, Machynlleth, Powys, SY20 8DQ

E	info@jpwconstruction.idps.co.uk	W	www.jpwconstruction.idps.co.uk/contact.html

IRELAND

Roman Szypura 3 Charles Street, Sligo, Co Sligo

T 	087 2389876

E 	roman@clioma.ie			W	 www.clioma.ie

Romac Acoustics, 10 Belgree Court, Killbride, Clonee, Co Meath

T 	087 2768668

Er	ronan@romac.ie		W

Fitzsimons Insulations Unit 55 Baldoyle Industrial Estate, Dublin 13

T 	01 8391111

E 	Peter@FITZIN.IE		W

Inform CA of selected applicator/installer at an early date.

Where possible select from local companies to support local economy and local employment.

See Preliminaries A90 Performance Specification A90/117.

509K	MATERIALS: Airtightness layers: MANUFACTURER & SUPPLIERS

Obtain materials of one type from only one source, unless specified or agreed otherwise in advance.

Obtain from only one of the following manufacturer(s)/fabricator(s)

Inform CA of selected manufacturer/fabricator at an early date.

Select from local companies to support local economy and local employment.

See Preliminaries A90 Performance Specification A90/117.

MANUFACTURER:

MOLL bauökologische Produkte GmbH, Rheintalstraße 35 – 43, D – 68723, Schwetzingen, Germany

ISO 9001:2000 by TUV Nord Cert GmbH, Germany.

Contact details are not included: All enquiries will be redirected to UK agents

IMPORTERS AGENTS SUPPLIERS:

England, Wales & Scotland Agent:

Ecological Building Systems UK Ltd.  17, City Business Centre, Lower Road, London SE16 2XB.

T	05600 758025	F	05600 758026

E	info@ecologicalbuildingsystems.com

W	www.ecologicalbuildingsystems.com

Contact: Penny Randell, UK Business Development Manager

M	0781 7896775

E	pennyrandell@ecologicalbuildingsystems.com

Ireland & Northern Ireland Agent:

Ecological Building Systems UK Ltd.  Main Street, Athboy, Co.  Meath, Ireland

T	00353 46 9432104	F	00353 46 9432435

E	info@ecologicalbuildingsystems.com

W	www.ecologicalbuildingsystems.com

ISO 9001

STOCKISTS/SUPPLIERS:

Construction Resources (Elink Ltd.) 111 Rotherhithe Street, London SE16 4NF, United Kingdom

T	020 7232 1181	F	020 7023 3789

E	General Enquiries	info@constructionresources.com

E	Sales / Request a Quotation	sales@constructionresources.com

W	http://www.constructionresources.com/default.asp

Contact: Richard Handyside

EcoMerchant Ltd. Head Hill Road, Goodnestone, Nr. Faversham, Kent, ME13 9BU

T	01795 530130

E	info@ecomerchant.co.uk	W	www.ecomerchant.co.uk

Green Building Store, Heath House Mill, Heath House Lane, Bolster Moor, West Yorkshire HD7 4JW

T	01484 461705	F	01484 653765

E	info@greenbuildingstore.co.uk 	W	www.greenbuildingstore.co.uk

Pen Y Coed Construction & Insulation Ltd.  Pen y Lan, Meifod, Powys, SY22 6DA

T	01938 500 797

E	info@penycoed-warmcel.com 	W	www.penycoed-warmcel.com

509L	Airtightness COMPONENTS: MANUFACTURER & SUPPLIERS

Obtain materials of one type from only one source, unless specified or agreed otherwise in advance.

Obtain from only one of the following manufacturer(s)/fabricator(s)

Inform CA of selected manufacturer/fabricator at an early date.

Select from local companies to support local economy and local employment.

See Preliminaries A90 Performance Specification A90/117.

MANUFACTURER:

Aico

T	0870 758 4000

E	Enquiries@aico.co.uk	W	www.aico.co.uk

W	http://www.aico.co.uk/Fire-Barriers.html

MOLL bauökologische Produkte GmbH, Rheintalstraße 35 – 43, D – 68723, Schwetzingen, Germany

ISO 9001:2000 by TUV Nord Cert GmbH, Germany.

Contact details are not included: All enquiries will be redirected to UK agents

IMPORTERS AGENTS SUPPLIERS:

England, Wales & Scotland Agent:

Ecological Building Systems UK Ltd.  17, City Business Centre, Lower Road, London SE16 2XB.

T	05600 758025	F	05600 758026

E	info@ecologicalbuildingsystems.com

W	www.ecologicalbuildingsystems.com

Contact: Penny Randell, UK Business Development Manager

M	0781 7896775

E	pennyrandell@ecologicalbuildingsystems.com

Ireland & Northern Ireland Agent:

Ecological Building Systems UK Ltd.  Main Street, Athboy, Co.  Meath, Ireland

T	00353 46 9432104	F	00353 46 9432435

E	info@ecologicalbuildingsystems.com		W	www.ecologicalbuildingsystems.com

ISO 9001

DESIGN

510	DESIGN/DESIGN DEVELOPMENT REQUIREMENTS:

512	AIRTIGHTNESS CHAMPION

Appoint an airtightness champion for the duration of the project, this need not be their only task but significant time must be allocated to the task at appropriate times.

Choose a person who is:

Full time

Based on site (site agent or project manager)

Interested in achieving airtightness or has past experience, reluctance is unlikely to lead to good will or good results.

Duties include:

Liaison with Project design team’s airtightness champion in design team meetings and on site.

Checking labour force for airtightness training or qualifications history

Organise any additional visits for “Upskilling for Airtightness training”

Facilitate or provide Airtightness tool box talks and video for airtightness and interface trades

Co-ordination of sequence, responsibilities and interface of trades on site

Development of checklists specific to project based on [________]

Facilitate airtightness intermediate checking, formal testing and any retesting

Photographic recording of all wind and air tightness work See P14/524

Recording failures into checklist, report back to all interface trades

Checking remedial action is understood and carried out.

Managing all paperwork associated with airtightness champion tasks.

515	DRAWINGS:

See work section A90

Tender Drawings to A90/120

Production Information Drawings: to A90/230-248

520	SPECIFICATION:

See work section A90

Tender Specification to A90/130,

Production Information Specification: to A90/250

522	METHOD STATEMENT:

See work section A90

Tender Method Statement to A90/170, 171

524	RECORD EVIDENCE OF WORK:

Keep a location log, cross referenced to digital photographic record of all surface junctions and service penetrations through the internal and external walls, partitions, floors, ceilings and roofs to show before, during and after evidence that they are sealed effectively and how.
Submit to CA as the work progresses.

If difficulties arise that require a change to the specification, materials or method, submit digital photographic evidence to CA and seek further instructions to meet the programme.

525	SAMPLES:

See work section A90

Tender Samples to A90/160,

Alternative Samples to A90/162

Samples: to A90/163

530	CONTROL SAMPLE

See work section A90

Control Samples to A90/166-168

PREPARATION

535	DELIVERY, STORAGE AND MARKING

Membranes are supplied in rolls.

Ensure:

Rolls are delivered on a pallet and shrink wrapped.

Accessories are

Each roll is labelled with a paper wrapper, which shows the manufacturer’s name, product description and production batch number identifying date and time of batch.

Product reference is printed on the exposed surface of the label and material.

Every roll shows the IAB identification mark and Certificate number and contains instructions on storage and installation.

Rolls are stored on end or laid flat

Rolls are kept under cover to protect from UV light.

Precautions:

Avoid contact with solvents and with materials containing volatile organic components VOC such as coal tar, and timbers newly treated with creosote.

Rolls must not be exposed to a naked flame or other ignition source.

540	PRE-INSTALLATION CHECKS:

Product Reference: Pro clima DB+ vapour check paper

Report any departures to the CA, do not commence until rectification by others is complete, ensure:

Insulation is installed between the rafters/joists/studs.

There are no gaps or chinks in the insulation and between the insulation and the rafters/joists/studs.

Wind tightness layer is installed on the outside/topside of the insulation.

No surfaces are frozen nor temperature is falling towards freezing point.

Timbers and insulation are not affected by or covered by moisture, frost, ice or mould.

Check timber member spacing and order roll width(s) to suit, to minimise waste.

Check abutment surfaces to determine type of sealant and size of sealing bead required for ordering quantities.

Noggins are available for fixing to support laps not occurring along framing members.

550	CURRENCY OF INFORMATION & METHODS:

Check with the agent’ technical helpline, See P14/509K, to ensure any technical developments are understood and included in the works.

560	CO-ORDINATION OF PROGRAMMES

Interface component installers:

Above and outside of framing:

Wind tightness membrane installed after insulation between framing

Between framing

Insulation installed between framing before airtightness membrane

Cables and wire to wall sockets, ceiling lights and other accessories

Water and gas pipes and drainage services

Blown-in insulation

Below and inside of framing

Carcass

Linings

Plasterboard drylining

Inside of masonry walls:

Plastering

Inform and co-ordinate with other installers, of the membrane installation programme to permit timely setting out and installation of services before, thermal insulation before or blown in thermal insulation after the membrane is substantially complete.

Ensure sealing of services apertures and insulation injection holes can be completed as quickly as possible afterwards to protect from moisture, water, wind,

Ensure covering up of membrane to protect form UV light.

During colder months, ensure vapour check and air-tightness layer are fitted and secured immediately after installation of the thermal insulation.

565	SOFTWOOD NOGGINS:

Co-ordination: co-ordinate with timber frame/roof sub-contractor

Provision: Ensure sufficient softwood noggins are provided free issue and left loose or lightly nailed to enable easy removal and re-fixing to suit.

Final positioning and fixing: [

By membrane sub-contractor to correspond with lap-joint positions.

By carpenter to membrane sub-contractor’s requirements]

Spacing: maximum 600 mm. centres but subject to IAB Certificate schedule.

570	PREPARATION:

During colder months, fit and secure the membrane immediately after installation of the thermal insulation.

Ensure all surfaces are suitable for permanent, airtight adhesion with air-tightness tape and joint adhesive, are stable, dry, smooth and free of dust, silicone and grease.

Ensure dust is vacuum cleaned or wiped off with a cloth.

Brush down surfaces before bonding.

NB.  Adhesion to frozen surfaces is not possible.

580A	PREPARATION: UNSTABLE OR CRUMBLING SURFACES:

Remove unstable or crumbling surfaces back to stable material

Grounding: [_____]

Stabilise surface using compatible stabiliser,

See P14/370B

APPLICATION: AIR TIGHTNESS

600A	APPLICATION:

Product Reference: Pro clima Intello Plus

The membrane has a front and back and must be fitted with the printed side facing the room/installer.

The printed markings are an aid to orientation and installation accuracy.

On the interior side, beneath the insulation, install the membranes:

In the case of a wall: working from head to base

In the case of a pitched roof: working from ridge to eaves,

The membrane may be unrolled and stapled either along or across the timber substructure members.

Ensure the membrane extends at abutment sufficient for movement and sealing see P14/610

Once the first membrane is in place, apply the second lapping layer

Always overlap the membranes on rafters/joists/studs/noggins to provide support for sealing.

Overlap the membranes:

with application of membrane across members:

end laps over timber members at least 100 mm.

side laps over noggins at least 100 mm.

with application of membrane along members:

end laps over noggins: at least 100 mm.

side laps over timber members at least 100 mm.

Lay the membrane without sagging but do not place under excess tension

Lay the membrane without creasing, as far as practicable.

Secure using staples: to P14/410A into timber backing members.

Pressure laths are usually not required on stable and unsupported surfaces.

601A	APPLICATION:

Product Reference: Pro clima DB+

The membrane has no front and back and can be fitted with either the printed or the unprinted side facing the room.

The printed markings are an aid to orientation and installation accuracy.

On the interior side, beneath the insulation, install the membranes:

In the case of a wall: working from head to base

In the case of a pitched roof: working from ridge to eaves,

The membrane may be unrolled and stapled either along or across the timber substructure members.

Ensure the membrane extends at abutment sufficient for movement and sealing see P14/610

Once the first membrane is in place, apply the second lapping layer

Always overlap the membranes on rafters/joists/studs/noggins to provide support for sealing.

Overlap the membranes:

with application of membrane across members:

end laps over timber members at least 100 mm.

side laps over noggins at least 100 mm.

with application of membrane along members:

end laps over noggins: at least 100 mm.

side laps over timber members at least 100 mm.

Lay the membrane without sagging but do not place under excess tension

Lay the membrane without creasing, as far as practicable.

Secure using staples: to P14/410A into timber backing members.

Pressure laths are usually not required on stable and unsupported surfaces.

610	SETTING OUT AND SECURING PERIMETER ABUTMENTS:

Ensure perimeter abutment joints can be sealed air-tight later.

Gable or jamb walls:

Ensure the membrane extends at abutment sufficient for movement and sealing

Wrap in excess material for expansion and fold into gap between perimeter abutment and closest framing member.

Allow about 30 mm. for sealing onto the abutment,

Initially fasten with staples if possible.

620	SEALING PERIMETER ABUTMENTS:

Jamb wall

Joint adhesives: Eco Coll: to P14/320A or Orcon F: to P14/322A

Apply directly from the cartridge in an pprox.. 5 mm. thick adhesive bead.

Apply to adjacent mineral/masonry structural components, plasterboard/plastered or rough wooden components

e.g. plastered walls or sawn timber.

On rough surfaces, increase the bead size as necessary.

Apply the membrane direct to the adhesive immediately and whilst the adhesive is still wet without applying excessive force.

Allow for movement of the parts, do not press the joint adhesive completely flat.

Tool: pressing aid See P14/390A

625A	SEALING LAPS:

Product Reference: Pro clima Intello: to P14/312A

Once the membrane is fitted, seal the overlaps:

Ensure lap joints are sealed air-tight.

Ensure bonding with adhesive tapes to the smooth printed side.

Seal membranes in the overlap area, without strain or loading,

Tape:

Internal or external: Tescon No. 1 See P14/332A

Internal only: universal adhesive tape Uni Tape See P14/330A.

Ensure joints occur on the framing members or fix noggins to suit.

Avoid creases in the membrane in the overlap area.

Any creases that do occur in the over-lap area must be cut off or the membrane relayed to remove creases.

Ensure creases are not taped over.

Apply the tape centrally over the joint and press down firmly

Tool: pressing aid See P14/390A

Delay between taping/sealing and air testing: Generally: 10 minutes minimum

625B	SEALING LAPS:

Product Reference: Pro clima DB+: to P14/311A

Once the membrane is fitted, seal the overlaps:

Ensure lap joints are sealed air-tight.

Seal membranes in the overlap area, without strain or loading,

Tape:

Internal or external: Tescon No. 1 See P14/332A

Internal only: universal adhesive tape Uni Tape See P14/330A.

Ensure joints occur on the framing members or fix noggins to suit.

Avoid creases in the membrane in the overlap area.

Any creases that do occur in the over-lap area must be cut off or the membrane relayed to remove creases.

Ensure creases are not taped over.

Apply the tape centrally over the joint and press down firmly

Tool: pressing aid See P14/390A

Delay between taping/sealing and air testing: Generally: 10 minutes minimum

630	CORNER SEALING

Ensure angled joints in membrane are made air-tight.

Use flexible corner adhesive tape Tescon Profil See P14/336A

Delay between taping/sealing and air testing: Generally: 10 minutes minimum

640	DOUBLE SKIN METAL FLUE PIPE

Background: double-skin insulated metal flue,

Apply pprox..  30 mm. of Pro clima DB+ membrane: to P14/311A to the metal surface

Apply pprox..  5 mm. thick adhesive bead (more if surface texture requires it) of Eco Coll: to P14/320A

Offer up the membrane, with excess materials to form an expansion joint,

Set membrane in adhesive bed.

Do not press the adhesive completely flat.

Seal the corners with short pieces of adhesive tape Tescon No. 1.  See P14/332A

Cut halfway through the adhesive tape pieces on the centre line, then apply shaping to the circular profiles.

Delay between taping/sealing and air testing: Generally: 10 minutes minimum

650A	TIMBER ROOF BEAM/RAFTERS:

Product Reference: Pro clima DB+: to P14/311A

Background: sawn timber beams or rafters,

Apply joint adhesive Eco Coll: to P14/320A in an approximately 5 mm. thick adhesive bead.

With rough background surfaces, increase the bead size as necessary.

Offer up the membrane with excess materials to form an expansion joint and fold accordingly.

Lay the vapour check in the adhesive bed,

Do not press the adhesive completely flat.

Delay between taping/sealing and air testing: 12 to 24 hours depending on weather conditions

660A	UNPLASTERED GABLE WALL INTERIOR:

Product Reference: Pro clima DB+: to P14/311A

Reference Detail: to P14/502 item 7, page 18

Plaster sealing tape: Contega PV: to P14/334A

Fix the fleece as far as possible in the corner using mechanical fixing or adhesive:

Mechanical fixings: Non-percussion drill, expanding or resin bolts, large head washers,

Adhesive: Orcon F: to P14/322A or Eco Coll: to P14/320A

Apply dabs of adhesive to the masonry or a bead of adhesive or using tacks at 400 mm. maximum.

Do not install the tape with a concave shape, fit tightly and neatly into corner

Offer up the membrane.

Remove the strips of release paper from the back of the Contega PV: to P14/334A

Fix the fleece to the membrane using adhesive tape, pressing firmly to secure.

Background: masonry walls to be plastered:

Suitable plaster types:

Gypsum bonding coat

Cement with a PVAC primer/adhesive

Lime with a PVAC primer/adhesive

Clay/loam plasters with a PVAC primer/adhesive

Ensure Contega PV: to P14/334A is embedded between coats of plaster.

Roll back the fleece and reinforcement away from the surface to be plastered.

Allow others to apply first coat of a suitable plaster to the wall

Unroll the fleece and reinforcement into the fresh layer of plaster

Allow others to complete the plaster work.

Delay between taping/sealing and air testing:

Generally: 10 minutes minimum

Orcon F: to P14/322A or Eco Coll: to P14/320A: 12 to 24 hours depending on weather conditions

660B	UNPLASTERED GABLE WALL INTERIOR:

Product Reference: Pro clima Intello: to P14/312A

Reference Detail: to P14/502 item 7, page 18

Plaster sealing tape: Contega PV: to P14/334A

Attach the tape using its self-adhesive strips to the smooth side of the membrane.

The white airtight fleece with the integrated blue plaster reinforcement mesh is then pushed back and fixed as far as possible into the corner,

Adhesive: Orcon F: to P14/322A

Apply dabs of adhesive to the masonry or a bead of adhesive or using tacks at 400 mm. maximum.

Background: masonry walls to be plastered:

Suitable plaster types:

Gypsum bonding coat

Cement with a PVAC primer/adhesive

Lime with a PVAC primer/adhesive

Clay/loam plasters with a PVAC primer/adhesive

Ensure Contega PV: to P14/334A is embedded between coats of plaster.

Roll back the fleece and reinforcement away from the surface to be plastered.

Allow others to apply first coat of plaster to the wall,

Unroll the fleece and reinforcement into the fresh layer of plaster

Allow others to complete the plaster work.

Delay between taping/sealing and air testing:

Generally: 10 minutes minimum

Orcon F: to P14/322A or Eco Coll: to P14/320A: 12 to 24 hours depending on weather conditions

665B	PLASTERED GABLE WALL INTERIOR

Product Reference: Pro clima Intello: to P14/312A

Background: plastered gable walls,

Apply adhesive directly from the cartridge in an approximately 5 mm. thick adhesive bead.

Adhesive: Orcon F: to P14/322A

With rough surfaces, increase the bead size as necessary.

Offer up the membrane, with excess material to form an expansion joint, fold in accordingly,

Lay the membrane in the adhesive bed.

To allow for movement of the parts, do not press the glue completely flat.

Pressure laths are usually not required on stable surfaces.

Delay between taping/sealing and air testing: 12 to 24 hours depending on weather conditions

665C	PLASTERED GABLE WALL INTERIOR

Product Reference: Pro clima DB+

Background: plastered gable walls,

Apply adhesive directly from the cartridge in an approximately 5 mm. thick adhesive bead.

Adhesive: Orcon F: to P14/322A or Eco Coll: to P14/320A

With rough surfaces, increase the bead size as necessary.

Offer up the membrane, with excess material to form an expansion joint, fold in accordingly,

Lay the membrane in the adhesive bed.

To allow for movement of the parts, do not press the glue completely flat.

Pressure laths are usually not required on stable surfaces.

Delay between taping/sealing and air testing: 12 to 24 hours depending on weather conditions

670	PIPES AND CABLES

Allow others to carryout setting out and fixing of services

Accurately cut the membrane at location of all pipe and cable penetrations, ensure the cut is no larger than required.

Allow others to securely fit and fix pipes or cables to accessories and surface boxes and or plates through the membrane.

Fit the correct size flexible grommet to each size of pipe and cable to ensure a tight fit and airtight seal

Push the grommet over the pipe or cable slide along length until in approximately the correct location(s).

Remove the release paper from the pipe and cable grommets, secure down to the membrane

Fix grommets using:

Internal or external: Tescon No. 1: to P14/332A

Internal only: Uni Tape: to P14/330A.

Press firmly to secure the adhesive tape.

Delay between taping/sealing and air testing: Generally: 10 minutes minimum.

680	BLOWN-IN INSULATION INJECTION & HOLES:

Allow others to create injection holes and complete injected insulation installation.

See work section P11.

Immediately after injection is completed, carryout injection hole repair, avoiding risk of injected insulation material loss at hole and moisture ingress.

681	INSULATION INJECTION HOLE REPAIR:

Patches: to P14/350A

Sealing tape: to P14/331A

Location: towards top of element that is insulated

Loading:

less pressure at top due to insulation,

pressure taken by pressure battens where required, See P14/421A

Application:

Attached tape to one edge of patch

Apply patch centrally to cover hole

Apply hand pressure to facilitate bond of tape to membrane, do not apply extreme pressure

Apply strips of tape to remaining three sides of patch to complete task

Delay between taping/sealing and air testing:

Generally: 10 minutes minimum

Orcon F: to P14/322A or Eco Coll: to P14/320A: 12 to 24 hours depending on weather conditions

682	DAMAGE REPAIR

Adhesive tape: Uni Tape to P14/330A

Patches: Uni Tape patch to P14/350A

Hole repair adhesive tape to P14/331A

685	VENTILATE REGULARLY TO PREVENT BUILD-UP OF EXCESS HUMIDITY:

Avoid build up of excess humidity in the building during the work.

Likely times of high humidity:

during periods of high precipitation: mist, fog, rain, snow, drizzle, etc.

during winter season,

during wet trade drying

Actions:

open window, permit cross ventilation

close windows and introduce ventilation

close windows and introduce dehumidification

690	AIRTIGHTNESS TESTING: INTERMITTENT TESTING:

Timing:

As rooms or parts of building are completed

Building fabric substantially complete

After service zone battening (if any) is complete

Before wall linings and surface finishes are complete

Purpose:

To check workmanship and integrity as the work progresses

To identify any difficult or problematic joints to be concentrated upon in subsequent works

Preparation:

Ensure all membrane connections have been made air-tight,

Ensure the thermal insulation system is sealed in,

Ensure all service penetrations are sealed

Ensure all damage is repaired

Seal any other structural openings related to tested space

Delay between taping/sealing and air testing:

Generally: 10 minutes minimum

Orcon F: to P14/322A or Eco Coll: to P14/320A: 12 to 24 hours depending on weather conditions

Check the air-tightness

Equipment: See P14/900A

Scope: Testing is possible for full rafter insulation if there are no other large openings in the building shell (i.e. when all windows have been installed), but not for testing with insulation above the rafters.

Method of test: use blower to exert negative pressure and detect air infiltration,

Keep records to enable carrying out of remedial actions.

695	ADHESION TESTING:

Delay between taping/sealing and testing:

Generally: 10 minutes minimum

Orcon F: to P14/322A or Eco Coll: to P14/320A: 12 to 24 hours depending on weather conditions

The best bonds are achieved against timber derived sheathing, prepared as described.

With other materials and in case of doubt, carry out adhesion tests.

Method of test: [___]

Test result pass level: [______]

APPLICATION: WIND TIGHTNESS

710	GENERAL

Product Reference: Pro clima Solitex Plus: to P14/317A.

Roof tile underlay must be installed and fixed in accordance with the Agrément Certificate, the manufacturer’s instructions, and the relevant recommendations of ICP 2:2002 and BS 5534-1:2003.

715	GENERAL INSTALLATION CRITERIA: ROOFING UNDERLAY

Product Reference: Pro clima Solitex Plus: to P14/317A

Roof tile underlay are not suitable for use in flat roof construction.

Where the length of the rafter slope measured on plan exceeds 6 m. roof tile underlay should not be used unless the manufacturer’s guidance is sought in relation to detailing.

Installation of roof tile underlay can be carried out in all conditions normal to pitched roofing work.

In roof construction it is important to remember that roof tile underlay are the second line of defence in excluding water penetrating the roof.

For this reason the following list of criteria must be met to comply with the requirements of the Agrément Certificate:

Ensure that roof tile underlay are correctly installed and not damaged.

Where roof tile underlay become damaged for whatever reason, it is imperative that they are suitably repaired with a new piece of matching material or a adhesive tape if the damage is minimal.

See Pro clima Tescon No. 1 P14/332A

720	INSTALLATION: ROOFING

Product Reference: Pro clima Solitex Plus: to P14/317A

During the operation of installing the roofing underslating:

Ensure that persons working on the roof do not use roof tile underlay for supporting themselves or the slates/tiles independently of the roof.

Provide overlaps of the roof tile underlay in accordance with the minimum dimensions given in ICP 2:2002.

See P14/110A.

725	INSTALLATION: ROOFING BATTENS & COUNTER BATTENS

Product Reference: Pro clima Solitex Plus: to P14/317A

Ensure batten gauges do not exceed that recommended by the tile/slate manufacturer for the particular tile/slate being used.

Ensure moisture content of battens at time of fixing do not exceed 22%.

Ensure that where overlaps do not coincide with a batten:

either include an extra batten at the overlap or

increase the underlay overlap to coincide with the next batten.

Seek manufacturer’s guidance in relation to chemical attack from wood preservative on roofing underlay.

The application of counter battens significantly reduces the risk associate with water penetration due to water ponding or by capillary action along the nail penetrations.

730	INSTALLATION: ROOFING UNDERLAY:

Product Reference: Pro clima Solitex Plus: to P14/317A

When tacking roof tile underlay to the rafters, use tack: to P14/411A or staples: to P14/410A

Ensure underlay is tacked at the head of the sheet only, at centres not exceeding 1200mm.

Ensure that all tacking nails are covered by the overlap of the next underlay course so that the minimum head-lap is maintained between the tacks and the lower edge of the overlapping underlay.

Where hips and valleys occur, they should be covered with an additional layer of underlay at least 750 mm. wide on each side, run continuously from eaves to ridge.

At ridge level, carry on roof tile underlay over the ridge.

Carryout correct detailing for ridge vents if the roof is ventilated, and a minimum overlap of 225mm.

Where roof tile underlay are fully supported on decking, counter battens must be used or where the architect/engineer specifies it to allow a deflection in the underlay to run the water into the gutter.

Roof tile underlay must be laid horizontally across the roof with the product name facing up.

Ensure that when installing roof tile underlay without counter battens in unsupported roofs, the roof tile underlay is draped with a deflection of 5-10 mm. between rafters to permit free drainage of water vapour into the gutter.

Ensure the deflection is not so great as to permit contact with the underside of the slating or tiling when the underlay is subject to wind uplift.

735	INSTALLATION: ROOFING VENTILATION:

Product Reference: Pro clima Solitex Plus: to P14/317A

Underlay may be installed without ventilation, however where ventilation is considered:

Ensure ventilation requirements are in accordance with TGD to Part F of the Building Regulations 1997 to 2006.

Ensure continuous ventilation is provided at a minimum rate equivalent to:

eaves ventilation: 10 mm./linear meter

ridge ventilation: 5 mm./linear meter

Incorporate a fly screen to prevent birds and insects entering the roof void.

Cold roof: proprietary eaves ventilators is strongly recommended as they ensure that quilt or loose fill insulation will not obstruct the flow of air where the insulation and roof meet. See P10/[____].

When using tile/slate ventilators they should be installed as close to the ridge as possible to increase ventilation circulation.

740	INSTALLATION VAPOUR CONTROL LAYERS:

Product Reference: Pro clima Solitex Plus: to P14/317A  roof tile underlay.

Where roof tile underlay are used in dormer roof construction, i.e. where the ventilation is along the line of the rafters, install a vapour control layer on the warm side of the insulation.

Materials:

See Pro clima Intello Plus vapour check P14/313A,

Non-ventilated cold roof design where the insulation is laid on top of the ceiling,

Include a sealed vapour control layer, such as Pro clima Intello Plus, on the warm side of the insulation.

Ensure all perforations for pipes, electrical cables etc. are sealed using Pro clima sealing accessories.

Ensure the vapour control layer is turned up around the edge of the insulation and sealed to the walls and soffit to inhibit warm humid air entering the attic.

Sealing:

Adhesive: Pro clima Orcon F: to P14/322A

Tape:  Tescon No. 1 tape P14/332A or Uni Tape: to P14/330A

For further guidance regarding sealing this detail, refer to manufacturer.

745	INSTALLATION EAVES:

Product Reference: Pro clima Solitex Plus: to P14/317A  roof tile underlay,

Roof tile underlay, if exposed to UV light on a continuous basis, will degrade;

At the eaves use waterproof underlay or eaves reinforcement sheet

Properties:

resistant to UV light

resistant to rot

Ensure the membrane is provided with a tilting fillet and is dressed 50 mm. into the gutter.

Where the UV resistant eaves protection sheet is dressed into the gutter, ensure it allows effective rainwater and water vapour drainage into the gutter but not affect the flow of rainwater in the gutter

Once the roof tile underlay is installed, ensure it is not exposed to UV light for more than 6 months as it will degrade.

750	INSTALLATION CRITERIA FOR NON-VENTILATED ROOF DESIGNS: CONDENSATION RISK:

Product Reference: Pro clima Solitex Plus: to P14/317A

Roof underlay have a significantly lower water vapour resistance than that of conventional roof underlay and therefore do not have to rely upon air movement beneath the underlay to minimise the risk of condensation.

However, it is essential that the amount of water vapour generated in the dwelling below is limited.

The following measures will help to reduce the build-up of water vapour:

Ensure all penetrations into the roof space are properly sealed

Ensure loft hatches are made convection tight by means of a compressible draught seal.

Provide airtight loft hatches: to P14/380

Ensure all other penetrations are sealed using Pro clima sealing accessories

Ensure the dwelling below the roof is ventilated in accordance with F1 of TGD to Part F of the Building Regulations 1997 to 2006 for the dispersal and rapid dilution of water vapour.

Ensure all water tanks in the loft space are covered and all pipe work lagged.

Ensure a sealed vapour control layer, is installed on the warm side of the insulation in both cold roof and warm roof designs.

See Pro clima Intello Plus vapour check P14/313A,

Ensure all penetrations, e.g. pipe work, electrical fittings, to the loft space are sealed using purpose made grommets or tapes.

See Pro clima rubber grommets: to P14/340A – P14/342A and P14/343A – P14/344A & P14/345A,

See Pro clima Tescon No. 1 flexible tape P14/332A

There is no requirement for eaves or ridge ventilation as both roof underlay do not require air movement to avoid damage by condensation.

760	NON-VENTILATED COLD ROOF:

In a non-ventilated cold roof, ensure the insulation is laid horizontally on the vapour check at ceiling level and is pushed into the eaves and against the underlay to ensure that there are no gaps present,

See Pro clima Intello Plus P14/313A

Ensure that a barrier to vapour movement is maintained on the warm side of the insulation over the whole ceiling.

Pay particular attention to the junction from the ceiling to the external wall.

Delay between taping/sealing and air testing:

Generally: 10 minutes minimum

Orcon F: to P14/322A or Eco Coll: to P14/320A: 12 to 24 hours depending on weather conditions

Test the integrity of the membrane using a blower door or Wincon tester prior to and post fixing of the internal lining(s). See: to P14/910 – P10/990.

770	NON-VENTILATED WARM ROOF:

Product Reference: Pro clima Solitex Plus: to P14/317A

In a non-ventilated warm roof, the insulation is installed between the rafters so as to fill the rafter void.

It is important to install the vapour check on the warm side of the insulation over the whole roof.

All laps, junctions to  adjacent structural elements and service penetrations of the vapour check should be sealed using suitable sealing accessories.

In a non-ventilated warm roof the underlay may be laid taut or draped, parallel to the eaves and fixed by counter battens (minimum thickness 25 mm.)

To increase the wind tightness of the roof, in the case of roofs with a low pitch, or in exposed areas, all overlaps, penetrations and junctions to adjacent structural elements of Solitex Plus or Solitex UD may be sealed using adhesive/tapes.

Application of Pro clima Solitex Plus shall be in accordance with BBA/IAB certificate application guidance details

See Pro clima Tescon No. 1: to P14/332A

COMPLETION

900A	TESTING EQUIPMENT: AIRTIGHTNESS QUALITY CONTROL UNIT IN CASING:

Airtightness Blower panel in casing

Controls & Magnahelic pressure gauge

Manufacturer: MOLL bauökologische Produkte GmbH, See P14/509K

Product Reference: Pro clima Wincon.

Performance 9800 m3/h at 50 Pa pressure differential to IS EN 13829:2000.

Voltage:

for construction site 110 V

for occupied building 220 V

CDM and Manual handling Regulations:

Weight: 30 kg. fan and 20 kg. box

Method statement: Provide a method statement on handling of equipment in excess of 20 kg.

905A	TESTING EQUIPMENT: AIRTIGHTNESS Blower Door:

Equipment: Airtightness Blower Door

Manufacturer: Minneapolis

Product Reference: Minneapolis Blower Door

Test method as Preliminaries section A94

Test level:

See A94/[____]

n50-Airchanges value: <[___] h-1 ([__] ACH at 50 Pa)

910	BUILDING USE AIR TIGHTNESS STANDARDS:

Based on ATTMA Technical Standard 1 Measuring Air Permeability of Building Envelopes

| Building Use | Air permeability m3/hr/m2 @ 50 Pa |  |  |
| --- | --- | --- | --- |
|  | Normal | Best Practice | Project requirement |
| Office |  |  |  |
| Natural ventilation | 7 | 3 |  |
| Mixed mode | 5 | 2.5 |  |
| Air Conditioning/low energy | 5 | 2 |  |
| Factories/Warehouses | 6 | 2 |  |
| Superstores | 5 | 1 |  |
| Schools | 9 | 3 |  |
| Hospitals | 9 | 5 |  |
| Museums and Archival stores | 1.5 | 1 |  |
| Cold Stores | 0.35 | 0.2 |  |
| Dwellings |  |  |  |
| Natural Ventilated | 9 | 3 |  |
| Mechanical ventilation | 5 | 3 |  |

920	AIRTIGHTNESS TESTING: FORMAL TESTING: PRE LINING COMPLETION

Timing:

Building fabric substantially complete

After service zone battening (if any) is complete

Before wall linings and surface finishes are complete

Preparation:

Ensure all membrane connections have been made air-tight,

Ensure the thermal insulation system is sealed in,.

Ensure all service penetrations are sealed

Ensure all damage is repaired

Seal any other structural openings

Delay between taping/sealing and air testing:

Generally: 10 minutes minimum

Orcon F: to P14/322A or Eco Coll: to P14/320A: 12 to 24 hours depending on weather conditions

Check the air-tightness

Equipment: See P14/905

Test level:

See A94/[____]

n50-Airchanges value: <[___] h-1 ([__] ACH at 50 Pa)

Method of test: use blower to exert negative pressure and detect air infiltration,

Keep records to enable carrying out of remedial actions.

925	REMEDIAL ACTION

Review surveys:

Infrared thermo graphic surveys see P14/930.

Review further inspection reports

Propose remedial actions and submit to the CA for review.

Participate in discussions on proposals, assist in decision making process.

Seek instruction to suit the programme

Carryout works as proposed/instructed.

Cease wind pressure whilst adhesives and tapes are applied and until they are set.

927	DELAY AFTER REMEDIAL ACTION BEFORE RETESTING:

Delay between taping/sealing and air testing:

Generally: 10 minutes minimum.

Orcon F: to P14/322A or Eco Coll: to P14/320A: 12 to 24 hours depending on weather conditions

930	INFRA RED TESTING:

See A90/156 & 156A and Preliminaries section A95.

Review test report and investigate anomalies for airtightness using air test and smoke stick to determine if lack of airtightness is the cause.

Record findings and co-ordinate with others via the Main Contractor to ensure others investigate unresolved anomalies.

950	TEST REPORT: See A90/151.

960	EXTERIOR CLADDINGS:

Protect membranes from damage and UV light.

Install within the manufacturer’s recommended time period, or 3 months maximum if less,

Allow others to install exterior cladding as early as possible after completion of testing, rectification and retesting.

Ensure claddings are fixed to battens to avoid puncturing membrane.

965	INTERIOR LININGS:

Protect membranes from damage and UV light.

Install within the manufacturer’s recommended time period, or 3 months maximum if less,

Allow others to install interior lining as early as possible after completion of testing, rectification and retesting.

Ensure linings are fixed to service battens to avoid puncturing membrane.

970	AIRTIGHTNESS TESTING: FORMAL TESTING: POST LINING COMPLETION

Timing:

Building fabric substantially complete

After service zone battening (if any) is complete

After wall linings and surface finishes are complete

Purpose: to check if the installation of linings has damaged the integrity of the airtightness membranes

Preparation:

Ensure all membrane connections have been made air-tight,

Ensure the thermal insulation system is sealed in,

Ensure all service penetrations are sealed

Ensure all damage is repaired

Seal any other structural openings

Delay between taping/sealing and air testing:

Generally: 10 minutes minimum

Orcon F: to P14/322A or Eco Coll: to P14/320A: 12 to 24 hours depending on weather conditions

Check the air-tightness

Equipment: See P14/905

Test method as Preliminaries section A94

Test level:

See A94/[____]

n50-Airchanges value: <[___] h-1 ([__] ACH at 50 Pa)

Method of test: use blower to exert negative pressure and detect air infiltration,

Keep records to enable carrying out of remedial actions.

975	REMEDIAL ACTION

Review surveys:

Infrared thermo graphic surveys see P14/930.

Review further inspection reports

Propose remedial actions and submit to the CA for review.

Participate in discussions on proposals, assist in decision making process.

Seek instruction to suit the programme

Carryout works as proposed/instructed.

Cease wind pressure whilst adhesives and tapes are applied and until they are set.

997	DELAY AFTER REMEDIAL ACTION BEFORE RETESTING:

Delay between taping/sealing and air testing:

Generally: 10 minutes minimum.

Orcon F: to P14/322A or Eco Coll: to P14/320A: 12 to 24 hours depending on weather conditions

980	TEST REPORT: See A90/151

990	CERTIFICATION: See A90/150

END OF WORK SECTION P14

© 2000-2009 NGS GreenSpec

REV	REVISIONS

| Revision No | Description | Author | Date | Checked by |
| --- | --- | --- | --- | --- |
| A00 | For Preliminary Issue Draft clause for DB+ for Construction Resources Clause used in numerous project specifications | BRM | 08/09/2008 | Never completed by CR |
| A01 | Complete rewrite for Ecological Building Systems Many clauses for 3 membranes and all accessories. Workmanship clauses and Guidance Notes First issue for comment | BRM | 11/05/2009 - 13/05/2009 |  |
| A02 | Text revisions throughout Added Intello & Intello plus text for comparison highlighting differences for new clauses Added Intello & Intello plus text for General guidance notes Restructure and renumber as separate work section P14 | BRM | 19/05/2009 - 02/06/2009 |  |
| A02 | Added Solitex SD & Solitex Plus text Other membranes added Added information from samples Created Appendix in file & literature Clauses renumbered throughout and Cross referencing completed Terms and conditions added Further information from material data sheets Ecological Building Systems commissioned clauses boxed | BRM | 02/06/2009 - 07/06/2009 |  |
| A03 | Training opportunities added Added other airtightness components Added Jargon Buster and emailed in separate file to P & N @ Ecological Building Systems UK Ltd. Change file name from P10_300A_SC_ProClimaDB+.doc: to P14_SWS_Airtightness_Working.doc Meeting 11/06/09 feedback substantially complete Prioritize Intello Plus, keep 3 Plus(s) and omit others (incomplete) | BRM | 09/06/2009 - 16/06/2009 |  |
| A04 | Mark up from meeting 30/06/09 Updating from PennyFeedback170709 email Updated from NiallFeedback070709 email Additional airtight socket insert Jargon Buster updated from A94, A95 & P14 Jarbon Busters Update from new brochure. Removed surplus text from old brochures and website Moved Jargon Buster to end | BRM | 17/06/2009 - 27/07/2009 |  |
| A05 | Rearrange clauses in order and revise Update Jargon Buster Merge in feedback from: NiallFeedbackEmail130809.html and P14_SWS_Airtightness_A04_270709Niall.doc Other completions Save copy | BRM | 02/08/2009 - 19/08/2009 |  |
| A06 | Remove all single strikethrough text Remove grey tone | BRM | 19/08/2009 |  |
| A07 | Pro clima UK mainland products only Edited down to Ecological Building System’s Specification only Red Text to Black Remove paragraph boxes Issue to Ecological Building Systems | BRM | 19/08/2009 |  |
| A08 from A06 | Feedback from NC mark up Add 3 more accessories to Ecological Building Systems set. Cross reference check Removed all grey tone Removed red text where safe to do so | BRM | 21/08/2009 |  |
| A09 | Pro clima UK mainland products only Edited down to Ecological Building System’s Specification only Remove paragraph boxes Issue to Ecological Building Systems | BRM | 21/08/2009 |  |
| A10 | Feedback from emails and marked up attachment from NC @ Ecological Building Systems EBS in full, Scope boxes updated, other updates | BRM | 28/08/2009 |  |
| A11 | Solitex UK marker added Alex W at CD2E Extracted Jargon Buster to separate file Extracted Guidance Notes to separate file Extracted Applicators & Installers and Suppliers & Manufacturers to separate file | BRM | 22/09/2009 - 14/12/2009 |  |
| A12 | Added 524 digital photographic surveys and log and added to 512 champion’s tasks minor editing. Added 505 video | BRM | 28/05/2011 |  |
| A13 | Renamed file, headers and footers, CAWS, URL update | BRM | 09/12/2012 |  |
| A14 | Updated URLs | BRM | 17/12/2012 |  |
| Pending | Add λ, add suitable backgrounds (where missing) Add rates for existing buildings Standards update | BRM | 28/05/2011 09/12/2012 |  |
| B00 | Reviewed, post on Website |  |  |  |

Terms and Conditions

1 The ‘Information’

1.1 The ‘Green Building Specification’ is a service provided by GreenSpec.  These terms and conditions may be revised from time to time without prior notice.

1.2 This draft specification was prepared for the GreenSpec ‘Green Building Specification’ by Architectural Specification Writing Services (ASWS).

1.3 The specification clauses in this document (the 'Information') are based on past project work, information gathered from seminars, workshops and assimilated from published or unpublished verbal and written information.

1.4 The Information will continue to be developed and current files will be maintained on the GreenSpec website at www.greenspec.co.uk

2 Copyright Notice

2.1 Copyright and all other intellectual property rights in the Information shall remain at all times the property of GreenSpec and you shall acquire no rights in any such material except as expressly provided in this Agreement.

2.2 You are permitted to reproduce any part or parts either alone or in conjunction with your own material for the purposes of internal use in the your office, or for inclusion in any drawings or contract documents used or intended to be used in connection with a building contract where you are contracting party, or in connection with which you are engaged by one of the contracting parties in a professional capacity.

2.3 You shall not use, sell, assign, rent, sub-license, loan, or otherwise deal in any way in the Information or any interest in it except as expressly provided herein.

3 Disclaimer

3.1 Whilst GreenSpec endeavours to ensure that the Information is correct, it is provided on an "as is" basis, without warranties of any kind, and no warranty, express or implied, is given as to accuracy, currency or completeness and GreenSpec does not accept any liability for any error or omission.  GreenSpec shall not be liable for any third party claims or losses of any nature including, but not limited to, loss of profits, direct, indirect, special or consequential damages arising from a third party's use or inability to use this Information.

3.2 All users and others must verify the contents of the Information and ensure that its application is effective to communicate what is required by them and that the Information is fit for their intended use which has not been specified by GreenSpec.

3.3 GreenSpec accepts no responsibility for the content on any internet website to which a hypertext link from this specification exists.  The links are provided "as is" with no warranty, express or implied, for the information provided within them.

4 General

4.1 If any part of this Agreement is held by a court of competent jurisdiction to be unenforceable the validity of the remainder of the Agreement will not be affected.

4.2 This Agreement is covered by the Laws of England and Wales.

______________________________________________________]

Addenda

NBS compatibility

National Building Specification (NBS) is the industry standard specification library.

GreenSpec’s Green Building Specification (GBS) is designed to complement NBS.

GreenSpec clauses are written specifically to address issues of environmental sustainability.

NBS adopts and develops the Construction Project Information Committee’s (CPIC) classification system Common Arrangement of Work Sections (CAWS) 1998 edition.

GBS adopts and develops the CPIC and NBS versions of CAWS to enable integration into NBS-based specifications.

GBS adopts NBS clause numbering to provide for easy clause assimilation.

CPIC: http://www.cpic.org.uk

CAWS: http://www.cpic.org.uk/en/publications/common-arrangement-listing.cfm

NBS: www.thenbs.com/