NGS National Green Specification

GBS Green Building Specification

NGS ROBUST SPECIFICATION

P10	SUNDRY INSULATION/PROOFING WORK/FIRE STOPS

To be read with Preliminaries A10-A55/General Conditions

PRODUCTS

136A	ACOUSTIC/THERMAL INSULATION SUPPORT TRAY:

Reference Drawing(s): ________

Locations: Timber/metal composite joist floors

Location(s): between metal web/timber composite floor joists

Performance:

Fire standard: LPS 1207

Strength, Water vapour permeability, Dimensional checks:

BBA Prototype Test Report: No. 5835 Date: 24/06/2009

Prototype Assessment:

BBA Prototype Report: M2/43465 date: 21/04/2010

Acoustics:

SRL Test Results: C/09/5L/20900/R01 Date: 12/10/2009

Compliance: Robust Details: E-FT-1, E-FT-2, E-FT-3,

Material: Recycled Polypropylene, double skin hollow cellular board

Purpose: support insulation and separate insulation from electrical cables and down lighters in voids

Manufacturer: Insumate Ltd. Unit 13 Skirsgill Business Park, Penrith, Cumbria, CA11 0FD, Wales

T	01768 866009

E	sales@insumateltd.com	W	www.insumateltd.com

Product Reference: Insumate 600 tray

Joist centres: 600 mm.

Joist width: [72/97/122] mm.

Size: [1200 x 528/504/478 x 140/160] mm.

Install: tray hung from [top of joist/top hat from bottom of joists/channel between sides of joists]

Fasteners: 2 No. metal staples per flange spaced apart

Other requirements: purpose made tab packers to bring tops of joists to constant level at sides and ends.

Product Reference: Insumate ES1 supports for narrow joist spacing.

Appendix/Clause(s) on previous page(s)

NB: NOTES ON EDITING SPECIFICATIONS:

Use as guidance, a stand alone appendix or merge into work section.

Delete all of the Information on this and other pages of guidance notes, excluding the page break above, down to the end of NBS compatibility URLs (website addresses), when adding this work section or clauses to a project specification or purchase order.

Edit the clauses by selecting the clauses required, deleting any not required, by editing the [blue text which often describes options available] within square brackets to suit the project; or edit the specification to suit the procurement method.

Remove all square brackets using search for [ and replace with nothing and search for ] and replace with nothing.

Replace blue text with black text by selecting all and choosing auto or black colour text.

There are clauses in Red text in the Specification these are examples of project specific versions of the generic clauses that are included for guidance and are likely to be deleted or edited if they are useful to the project.

Remove any grey tone by selecting all text, and select Format > Borders and Shading > Shading > No fill > Okay.

© 1985-2013 ASWS NGS BrianSpecMan

REV	Revisions

| Revision No. | Description | Author | Date |
| --- | --- | --- | --- |
| A00 | Extracted from P&M Dale farm Cambridge Spec and neutralised For DRAFT issue to post on website for review | BRM | 16/01/2015 |
|  | Pending |  |  |
|  | Reorganise to Uniclass 2012 elemental classification |  |  |

Terms and Conditions

1 The ‘Information’

1.1 The ‘Green Building Specification’ is a service provided by NGS. These terms and conditions may be revised from time to time without prior notice.

1.2 This draft specification was prepared for the NGS ‘Green Building Specification’ by Architectural Specification Writing Services (ASWS).

1.3 The specification clauses in this document (the 'Information') are based on past project work, information gathered from seminars, workshops and assimilated from published or unpublished verbal and written information.

1.4 The Information will continue to be developed and current files will be maintained on the NGS website at www.greenspecdownload.co.uk

2 Copyright Notice

2.1 Copyright and all other intellectual property rights in the Information shall remain at all times the property of NGS and you shall acquire no rights in any such material except as expressly provided in this Agreement.

2.2 You are permitted to reproduce any part or parts either alone or in conjunction with your own material for the purposes of internal use in the your office, or for inclusion in any drawings or contract documents used or intended to be used in connection with a building contract where you are contracting party, or in connection with which you are engaged by one of the contracting parties in a professional capacity.

2.3 You shall not use, sell, assign, rent, sub-license, loan, or otherwise deal in any way in the Information or any interest in it except as expressly provided herein.

3 Disclaimer

3.1 Whilst NGS endeavours to ensure that the Information is correct, it is provided on an "as is" basis, without warranties of any kind, and no warranty, express or implied, is given as to accuracy, currency or completeness and NGS does not accept any liability for any error or omission. NGS shall not be liable for any third party claims or losses of any nature including, but not limited to, loss of profits, direct, indirect, special or consequential damages arising from a third party's use or inability to use this Information.

3.2 All users and others must verify the contents of the Information and ensure that its application is effective to communicate what is required by them and that the Information is fit for their intended use which has not been specified by NGS.

3.3 NGS accepts no responsibility for the content on any internet website to which a hypertext link from this specification exists. The links are provided "as is" with no warranty, express or implied, for the information provided within them.

4 General

4.1 If any part of this Agreement is held by a court of competent jurisdiction to be unenforceable the validity of the remainder of the Agreement will not be affected.

4.2 This Agreement is covered by the Laws of England and Wales.

______________________________________________________

Addenda

NBS compatibility

National Building Specification (NBS) is the industry standard specification library.

NGS’s Green Building Specification (GBS) is designed to complement NBS.

NGS clauses are written specifically to address issues of environmental sustainability.

NBS adopts and develops the Construction Project Information Committee’s (CPIC) classification system Common Arrangement of Work Sections (CAWS) 1998 edition.

GBS adopts and develops the CPIC and NBS versions of CAWS to enable integration into NBS-based specifications.

GBS adopts NBS clause numbering to provide for easy clause assimilation.

CPIC: http://www.cpic.org.uk

CAWS: http://www.cpic.org.uk/en/publications/common-arrangement-listing.cfm

NBS: www.thenbs.com/