## Slide 1: Lecture: Adopt a material Advanced Technology Module Leader: Ilona Hay Technology Campion: Brian Murphy Presented: 16th October 2018 Updated: 17th October 2018

## Slide 2: Material Groups
C01 C02 Ceramics
F01 F02 Found Objects
H01 H02 Hand Tools
P01 P02 Plaster
T01 T02 Timber
TX01 TX02 Textiles

## Slide 3: Your task: collate & record
How it is made
  Raw materials, preparation, process, end product
Inherent Properties
  Strength, weakness, construction considerations
Sustainability
  Sourcing, production process, pollution caused, carbon footprint, recycling
Relevant Precedent Studies
  Construction principles, typologies, details
Comparative Qualities
  Compare with the other material groups
Design process
  Sketches, drawings, prototypes, tectonics, fabrication

## Slide 4: C01 C02 Ceramics
Starts as Clay from the ground
  Excavated subsoil (inert) below topsoil (alive)
  Blended: clays, straw reinforcement, fine sand aggregate, sawdust, mineral dyes
  Format: bricks, block, rammed earth, cob
  Wooden moulds, clay thrown into brick mould,
  Extruded and wire cut into bricks
  Can have texture added by roller
  Common bricks can have sand added to face
  Small balls into formwork and rammed in 75 mm layers squeezed to 50 mm visible layers
  Loadbearing
    But susceptible to thermal/moisture movement

## Slide 5: C01 C02 Ceramics
Can be sun/air dried: moisture driven off
  Solar energy intensive but free and no carbon
  Sets dry but no curing nor strengthening
  Can be softened with water or steam
  Can reabsorb moisture vapour moderating humidity, avoiding need for ventilation or air conditioning

## Slide 6: C01 C02 Ceramics
Can be fired (cooked)
  High temperature, Energy intensive,
  Carbon level depends on fuel choice
  Clays can have an inherent fuel gas released by heat during firing but flue emissions increase
  Can be glazed (colour coated) for first firing
Can be double fired
  Terracotta: glazed for second firing
  Glazes: Matt to Gloss and big colour range
    Including mimicking stone

## Slide 7: C01 C02 Ceramics
Formats:
  Bricks, Glazed Bricks, Blocks,
  Floor/wall Tiles, Glazed tiles, Roof tiles
  Rain screen extrusions
  Ornate Sculpture (mimicking stone carving)
Early form of mass production
  Stone masons or clay modelers carved ornate pieces,
  Moulds made or taken, many copies made in terracotta
Terracotta hollow blocks
  filled with lightweight aggregate with cement matrix
Lightweight extruded hollow blocks
  insulating voids and long pathways make good U values
Crushed brick:
  consolidated hardcore, piling mat, brown roof gravel

## Slide 8: C01 C02 Ceramics
Loadbearing capacity
  Increases with firing temperature
  And choice of clay
  Formation of structure: walls, timbrel arch,
Moisture permeable: especially with lime mortar jointing
Water resistant: with cement mortar used as 3 course bricks DPC
  Engineering brick Damp Proof Course with strong cement mortar
Acoustic properties due to mass
Fire Resistant due to firing
Thermal mass due to density: Good
Thermal insulation: winter heat loss (conductivity k value): Poor
Decrement Delay: summer solar radiation protection
  Thick walls: long delay
  Thin roof tiles: little protection
Floor and wall tiles:
  Strong, tough, easy-clean,
  Water or chemical-resistant (Grouting performance to match)
  Slip resistance: Glazed tile slip, unglazed grip
    depends on footwear: Rubber boots grip, bare feet may slip

## Slide 9: C01 C02 Ceramic
Rammed Earth Wall
  https://www.pinterest.co.uk/bmurphy1390/rammed-earth-wall/
Cob
  https://www.pinterest.co.uk/bmurphy1390/cob/
Brickwork
  https://www.pinterest.co.uk/bmurphy1390/f10-brickwork/
Mortar
  https://www.pinterest.co.uk/bmurphy1390/z21-mortar/
Roof wall tiles
  https://www.pinterest.co.uk/bmurphy1390/h6-slating-tiling-roofing-cladding/
Timbrel Arch
  https://www.pinterest.co.uk/bmurphy1390/timbrel-arch-construction/

## Slide 10: F01 F02 Found Objects
Which materials: [_______________________________]
How it is made
  Raw materials, preparation, process, end product
Inherent Properties
  Strength, weakness, construction considerations
Sustainability
  Sourcing, production process, pollution caused, carbon footprint, recycling
Relevant Precedent Studies
  Construction principles, typologies, details
Comparative Qualities
  Compare with the other material groups
Design process
  Sketches, drawings, prototypes, tectonics, fabrication

## Slide 11: F01 F02 Found Objects
Scope:
  Circular economy (dismantled building parts)
  Architectural Salvage (Hand crafted)
  Construction reclaim (others components)
  ‘Dumpster diving’ (with owners permission)
    (surplus to requirements, off-cuts, damaged)
  Materials Exchanges (surplus to requirements)
  Local Resource Locator websites
  Surplus to requirements, Returned to stock
  Industrial process waste: eg. lazar cut waste

## Slide 12: F01 F02 Found Objects
Environmental impacts:
  Historic manufacture (so impacts ignored?)
  LCA Life Cycle Analysis (impacts apportioned to main product and bi-product or co-product)
Reclaimed Product Quality:
  Product Passport from first life/use
    Based on Product Specification
  See BAMB EU Horizon 2020 funded Project
    Buildings as Material Banks www.bamb2020.eu
    https://passports.bamb2020.eu
    User name: guest password: bambplatform

## Slide 13: F01 F02 Found Objects
Size is everything
  Ideally modular and consistently so
  Designed to reduce waste in first use
  Design with the same in mind or waste more in second use
Fixing methods is fundamental
  Design for ease of assembly, dismantling and reassembly
  State of repair in fixing zone
  Take care of buried ‘lost’ fasteners
    They will wreck your tools: saws and drills
    Companies with big magnets extract fasteners

## Slide 14: F01 F02 Found Objects
Lazar cutting scraps v efficiency iterations
https://www.pinterest.co.uk/bmurphy1390/resource-effective-design/

## Slide 15: H01 H02 Hand Tools
Which tools: [_________] Which materials: [______________]
How it is made
  Raw materials, preparation, process, end product
Inherent Properties
  Strength, weakness, construction considerations
Sustainability
  Sourcing, production process, pollution caused, carbon footprint, recycling
Relevant Precedent Studies
  Construction principles, typologies, details
Comparative Qualities
  Compare with the other material groups
Design process
  Sketches, drawings, prototypes, tectonics, fabrication

## Slide 16: Hand Tools/ Hand crafted materials
Clay: See C01 C02 Ceramics above
Plaster: See P01 P02 Plaster below
Timber: See T01 T02 Timber below
Textiles: See TX01 TX02 Textiles at end
Metals: See next
Machining Materials: See after Metals

## Slide 17: Metals
Metals
  https://www.pinterest.co.uk/bmurphy1390/z11-metals/

## Slide 18: Machining Sheet Materials
Lazar cutting
  https://www.pinterest.co.uk/bmurphy1390/lasar-cutting/
CNC Milling
  https://www.pinterest.co.uk/bmurphy1390/cnc-millingcutting/
Resource Efficiency
  Lazar cutting scraps v efficiency iterations
  https://www.pinterest.co.uk/bmurphy1390/resource-effective-design/

## Slide 19: P01 P02 Plaster
Materials:
  Clay,
  Horse manure, grass stem reinforced
  Lime: Derived from Limestone (UK) or marine shell (Holland)
  Cement: OPC, GGBS or blended
  Gypsum, Desulferisation gypsum (power station flue gas filtering)
  Diatomacious Earth (prehistoric ocean floor sediment)
Ingredients:
  Bulking/Strengthening/texture/colour: Sand and fine aggregate
  Reinforcement: horse hair, hemp shiv,
  insulating aggregates: Cork granules, hemp shiv,
  Pigments: minerals
Mixes:
  Cement/lime/sand,
  Lime/clay/diatomaceous earth/cork granules
  Hemp/lime, Hemp/lime/cement/aluminium oxide

## Slide 20: P01 P02 Plaster
Backing/Substrate:
  Solid walls:
    Masonry with raked joints for key
  Cast concrete with hessian in formwork
    Smooth concrete may need primer
  Wattle and daub
    oak strips weaved and lime plaster
  Metal meshes for gypsum plaster
Application:
  By hand: leaving hand and finger prints
  Mortar board > trowel > backing then trowelled smooth
  Projection: render flicked onto backing: good bond, peaky texture
  Pebble dash: texture and colour pebbles added to peaky surfaces
  Pumped through hose: smoothed by trowel
  Parge coats: airtight before plasterboard
  Plaster: airtight without plasterboard
  Wet trade requires time to dry before following trade (paint)

## Slide 21: P01 P02 Plaster (internal)
Properties:
  Clay: see C01 C02 Ceramics: (Unfired only)
    Internal only (unless protected from weather)
    Moisture mass: moderates humidity
    Absorbs smells, good for bathrooms
    Absorbs electromagnetic radiation (wifi etc)
    High density: adds thermal mass
    Low skill and strength needed, DIY repairable
    Add mineral dye; clay skim coats
    Inert waste, add back to soil?

## Slide 22: P01 P02 Plaster (internal) Render (external)
Properties:
  Lime:
    Alkali: Dangerous in the wrong hands (Not DIY)
    Active waste: in landfill until hydrated, set and strengthened
    Anti bacteria
    Moisture mass: moderates humidity
    Moisture permeable, moisture transport
    Some carbon sequestration from atmosphere
    Weaker than cement, flexible,
    Reclaimable and recyclable (adding heat)
    Medium density: medium thermal mass

## Slide 23: P01 P02 Plaster (internal) Render (external)
Properties:
  Cement:
    High embodied energy and carbon
      (8-10% of manmade carbon dioxide)
    Stronger than lime, less flexible, less forgiving
    Water and water vapour resistant
    Traps water in walls with no way out
      Saturates embedded timbers leading to rot and structural failure
    Never use cement anywhere on or in historic buildings (pre 1919)
    Inert waste in landfill once set

## Slide 24: P01 P02 Plaster (internal)
Properties:
  Gypsum: (internal)
    Lower embodied energy and carbon
    Water and water vapour resistant
    Traps water in walls with no way out
      Saturates embedded timbers leading to rot and structural failure
    Avoid gypsum plaster inside external walls in historic buildings (pre 1919) (use lime or clay)
    Stable Non-Reactive Hazardous waste in landfill (equivalent to asbestos for different reasons)
      Potential to react with landscape waste
      Release sulfer to atmosphere making acid rain
      More expensive to dump so use it wisely

## Slide 25: P01 P02 Plaster
Performance & Application:
  Hemp-lime:
    Insulating Render/Insulating Plaster
  Applied very thickly 300 mm not unusual
  Slow to set, hydrate, strengthen
    Ultimate Strength: Less than 3 kN/m2
  Once fully hydrated (>1 year) performs far better than predicted.
  Off site air drying can speed up process
  Exhibits a phase change characteristic
  Some add:
    Cement for fast initial set and drive the lime to hydrate faster
    Aluminium oxide to react with cement and foam up for insulation function

## Slide 26: P01 P02 Plaster
Performance and Application:
  Diatomacios earth/clay/lime/cork granules:
  Insulating:
    External Render, Internal Plaster, Floor Screed
  Airtight application, smooth or textured finish
  High thermal mass
    High decrement delay
    Summer solar protection
  Moisture Permeability (moisture escapes)
  Hygroscopicity (Moisture buffering)
  Thicknesses: 40-100 normal
    much thicker possible
  Value engineering: One-coat one-trade multi-functional multi-performance finish

## Slide 27: P01 P02 Plaster
Render
  https://www.pinterest.co.uk/bmurphy1390/m21-external-insulation-with-rendered-finish/
Cob
  https://www.pinterest.co.uk/bmurphy1390/cob/

## Slide 28: T01 T02 Timber
Raw materials: (A seasonal crop)
  Hardwood: Deciduous, Broadleaf
  Softwood: Coniferous, Pine needs and cones
  Moonwood: winter: low sap, night time, least moon gravity, (sacred in some societies?)
Manufactured:
  Glulam Glued laminated wood: frames
    (strength where its needed, weaker where it is not)
  LVL Laminated Veneer Lumber
    (using thinnings, thin layers same direction)
  CLTP Cross Laminated Timber Panels
    (using thinnings, softwood/plywood in layers)
  Other compound sections

## Slide 29: T01 T02 Timber
Timber Panel Products:
  Plywood: thin leafs of wood, glued layers, layers at right angles
  Particleboard:
    Chipboard (chips),
    OSB (shavings),
  Wood fibre boards,
    MDF Medium density fibreboard,
    medium board,
    hardboard
  Wood fibre Insulation boards and batts
    Breathing, sheathing, thermal + acoustic insulating

## Slide 30: T01 T02 Timber
Ingredients:
  Treatment: (killing chemistry)
    Preservatives, Fire protection,
    rot resistant, insect resistant
  Salts: added to recipe
    offering any of above treatments
    Borax mineral (as benign as possible)
  Heat Treatment: Remove nutritional content for Durability

## Slide 31: T01 T02 Timber
Assembly:
  Geometry, mechanical connection, friction, gravity
  Adhesives:
    Historic: animal glue;
    Modern: synthetic high performance
  Fasteners:
    Historic: Hardwood Dowels,
    Modern: Metals, plastic, chipboard biscuit,

## Slide 32: T01 T02 Timber
Grown:
  Photosynthesis: nature converting sunlight and Carbon dioxide into cellulose and oxygen (great synergy with humans)
  Carbon Dioxide Sequestration = Carbon negative
  Low energy input with carbon based petrol chain saws
  Transport emissions or floated down rivers, if not remote
Source:
  Forests: but ideally very selectively leaving forest intact
  Plantations: thinnings or the final crop
  Replanting more trees not palm oil: Sustainable management
Certified Sustainable:
  looking after nature and indigenous people
  FCS Forest Stewardship Council ‘or equivalent’
    Chain of Custody: Plantation > Joiner or Plantation > Building site
  Certified legal: Just got easy
  EUTR EU Timber Regulations EU Funded Project
  www.nepcon.org/sourcinghub

## Slide 33: T01 T02 Timber
Processing:
  Debarked (cork comes from bark)
  Sapwood removed (Perishable recently living, with sap flowing in the veins)
  Heartwood saved (durability resides here)
  Sawing, cutting arrangement (waste in sawdust and scraps)
  Planing, leaving rough or adding texture
  Waste scraps: fuel or into timber panel products
  Machining Energy’s carbon: reduces the carbon negativity of timber (but not a lot)

## Slide 34: T01 T02 Timber
Properties
  Durability:
    depends upon species
    will change if grown in different climates
    is classified and applicable to end use
  Grain:
    give strength in one direction and weakness in others
    figuring is not always the same as grain
  Machine able to varying degrees:
    grain direction dictates, craftsmen know-how
  Designers/Engineers exploit grain direction
  Manufacturer invent products to solve weaknesses

## Slide 35: T01 T02 Timber
Connecting Hand made joints
Paul Sellers does a fine job of a Mortice and Tenon joint in 30 minutes, very detailed commentary
  https://uk.video.search.yahoo.com/yhs/search?fr=yhs-imt-brwsrex&hsimp=yhs-brwsrex&hspart=imt&p=mortice+and+tenon+joint+video#id=1&vid=6373eb34d00240e8cc58fdd3b7a112dc&action=click
Drawbored M&T joint with very different approach in 10 minutes, with the magic touch at the end
  https://uk.video.search.yahoo.com/yhs/search?fr=yhs-imt-brwsrex&hsimp=yhs-brwsrex&hspart=imt&p=mortice+and+tenon+joint+video#id=6&vid=76f979695f3693e3545e83b045019817&action=view
And some serious 3D dovetails and a whole lot more in 16 minutes
  https://www.youtube.com/watch?v=0kgCsZJGluc

## Slide 36: T01 T02 Timber
Connecting: Fixings Fastenings
  https://www.pinterest.co.uk/bmurphy1390/z20-connectivity/
Timber Structure
  https://www.pinterest.co.uk/bmurphy1390/g20-timber/
Timber
  https://www.pinterest.co.uk/bmurphy1390/z10-purpose-made-joinery/
Shingles and Shakes
  https://www.pinterest.co.uk/bmurphy1390/h64-shingles-shakes/
Plywood furniture
  https://www.pinterest.co.uk/bmurphy1390/n20-plywood-furniture/

## Slide 37: TX01 TX02 Textiles
Scope:
  Carpet/rugs, underlays,
  Hung fabrics
  Stretched fabrics,
  Furniture upholstery,
  Geotextiles,
  Recycled fabric insulation (denim, cotton)
Materials:
  animal wool/hair: sheep’s wool,
  insect: cotton, spiders web, silk,
  Animal or fish leather,
  Synthetic plastics, Bio-plastics
  Blends of natural and technical/synthetic
    (contrary to Cradle to Cradle C2C principles)

## Slide 38: TX01 TX02 Textiles
Ingredients: Sheep dip (historic but might persist), animal droppings, tangles, thorns, seeds/husks, insect eggs,
Process: separating, washing, carding, combing, dying, weaving, trimming, edging, sewing
Impacts: unhealthy dip, waste, chemically intensive dying, water polluting, waterway/waterbody polluting.
Additional treatments: moth deterrent, fire treatment in upholstery

## Slide 39: TX01 TX02 Textiles
Weaving gives strength, texture, pattern, rhythm, colours
Different weaves make fabric hang/flow/stretch/shrink/hug differently
Treatments improve: fire properties, durability
Some moth killer treatments:
  CNS Central Nervous System depressants
  Invented by Germans to kill British in WW World Wars
  Now we douse our carpets and fabrics

## Slide 40: TX01 TX 02 Textiles
Applications & Performance:
Carpet: Thermal insulation: Thermal Comfort, Acoustic: Absorption, Tactile
Curtains: Solar control, Privacy, Black out, Draft lobby at doors, Thermal insulation at windows, Fire resistance (Stage curtain)
Wall and Ceiling linings: Decoration, Colour, Acoustic Absorption, may need to be low surface spread of flame and non-combustible
Furniture: Linings, Upholstery (fire/smoke propeties)

## Slide 41
Another GBE CPD/Lecture file to download
And https://greenbuildingencyclopaedia.uk

## Slide 42: Sampler
This is a cut down version of the original file to give you a sample of the whole
It’s the front end of the file with the middle and rear end deleted
Go tohttp://GreenBuildingEncyclopaedia.uk
to down load the whole file
You will find a large number of other files there too

## Slide 43: Feedback
These files are created by generalists with a big dollop of green flavour
These files are updated from time to time
We are not experts so from time to time these file may get out of date or may be wrong.
If you feel that we have got it wrong please let us know so we can put it right

## Slide 44: © GBE 2018
Brian Murphy BSc Dip Arch (Hons+Dist)
  Architect by Training
  Specification Writer by Choice
  Environmentalist by Actions
Greening up my act since 1999
Founded National Green Specification 2001
Launched www.greenspec.co.uk 2003
Created: GBE at https://greenbuildingencyclopaedia.uk 2015
E BrianSpecMan@icloud.com
Twitter: http://twitter.com/brianspecman
Twitter: GBEGreenBuild @GBEGreenBuild
Scribd: BrianSpecMan
LinkedIn: BrianSpecMan
Facebook: BrianSpecMan Facebook: http://www.facebook.com/brianspecman
Google+: BrianSpecMan • BrianSpecMan CAPEM • NGS National Green Specification
Slide Share:
Pinterest: Brian Murphy • GBE Green Building Encyclopaedia
CAP’EM: GreenSpec & NGS
CAP’EM Compass
LSBU London South Bank University Faculty and Course website page Brian Murphy